## Slide 1: Simulation of 10BASE-T1S Link Partner
Student: Tanner Fortier
Advisor: Dr. Messner

## Slide 2: TABLE OF CONTENTS 1. 5.
Motivation
Reasoning behind the project
Reanalysis of Design
Simplification of our approach and design
Overview
Explanation of project and its components
2.
Validation of Waveform
Testing components of project
6.
Approach
Thought process behind completing the project
3.
Overall Status
What has/needs to be completed
7.
Waveform Development
Process of building necessary bit stream
4.
Future Work
Additional applications and use cases
8.

## Slide 3: Motivation
Interoperability Lab
Conformance Testing
Automotive Industry and Industrial Automation
Short reach multidrop

## Slide 4: Overview
Software
MATLAB
NI-VISA (SCPI Implementation)
Mechanical System
Siglent SDG6000X
10BASE-T1S compatible device
Oscilloscope
Probes

## Slide 5: Approach
Review IEEE Clause 147
Operation of 10BASE-T1S Phy
IEEE 2 Level Differential Manchester Encoding, 4B5B encoding, 17 Bit Self Synch. Scrambler
Analyze state diagrams

## Slide 6: Waveform Development
Utilize MATLAB to build waveform
4B5B encoder/decoder
17 Bit scrambler/descrambler
DME encoder/decoder to offer better clock recovery

## Slide 7: Reanalysis of Design
17bit self synchronizing scrambler not necessary
Operating under specific conditions
Device in slave mode without auto-negotiation
Possible to build waveform without 4B5B encoder
Rebuild waveform

## Slide 8: Validation of Waveform
Upload waveform to AWG
Verify output on oscilloscope
Utilize logic detection to find specific codeword
DME Encoded “HEARTBEAT”

## Slide 9: Overall Status
DME Development: Completed
Waveform Development: Completed
Test Output Waveform: Completed
Test on Vendor Device: Not Completed

## Slide 10: Future Work
Support for both master and slave operation
Half-duplex support – packet level implementation
Auto-negotiation support
Support for other SPE technologies