## Slide 1: Dual-Axis Solar Tracker
Electrical and Computer engineering
ECE 792: Senior Project II
By: Kyle Beaupre
Advisor: Professor Edward Song

## Slide 2: Introduction: Nonrenewable Energy
Fossil fuels account for roughly 80% of U.S. energy production
Fossil fuels are energy efficient, but cause pollution
There have been strides towards new energy sources that are easily replaceable and less harmful to the environment

## Slide 3: Introduction: Renewable Energy
Most common renewable energy sources are wind, solar, hydroelectric, and geothermal
Renewable energy accounts for roughly 10% of U.S. energy production
This is because renewable energy sources are inefficient or difficult to implement
Renewable energy production needs to significantly increase to meet nonrenewable energy production

## Slide 4: Solar Energy: Disadvantages
Today's solar panels are roughly 22% efficient
Solar energy is not consistent
Solar panel inefficiency is influenced by temperature, time of day, and location

## Slide 5: Solar Energy: Advantages
Solar energy is currently the most obtainable form of renewable energy
Cheap
Easy to install
Maintenance cost are minimal
Operating costs are minimal
Increasing efficiency, or maximizing output potential, could allow solar energy to compete with nonrenewable energy

## Slide 6: Solar Panels
Solar panels are made up of groups of solar cells called modules
Solar cells convert sunlight into electricity
Solar cells consists of a semiconductor, an antireflective coating, and front and back contacts.
As sunlight touches the cell, electrons are removed from atoms and electricity is generated

## Slide 7: Solar Tracking
Stationary solar panels do not always receive the maximum possible concentration of sunlight
As the earth rotates, the position of the sun changes in the sky
The best way to maximize potential is to assure solar panels are always orientated towards the sun as the day progresses
A dual axis solar tracker will be constructed to determine increase in power production between a rotating solar panel and a stationary solar panel

## Slide 8: Dual Axis Solar Tracker Components
Small solar panel with USB output x2
DC portable battery x2
USB multimeter x2
Dual axis servo motor: Raspberry Pi Servo Motor Controller PWM Kit
Microcontroller: Raspberry Pi 3 Model B+
Motor controller: PCA9685
Camera: PiCamera NoIR

## Slide 9: Summary
Fossil fuels are efficient but harmful to the environment
Clean energy, such as solar, is inefficient
Further innovations in solar energy are needed if it will ever replace fossil fuels
A way to maximize the efficiency of solar panels is to track the sun
A dual axis solar tracker will be constructed
The average power production of the device will be determined and compared to a stationary device

## Slide 10: Prototype

## Slide 11: Testing
Testing was constrained to ten total days due to time, travel and environmental constraints
Both the solar tracker and fixed solar panel were tested at the same time
Testing took place during various weather conditions and temperatures
The solar panels were placed in the same location everyday
The measurements were taken hourly for twelve hours each day

## Slide 12: Data: Solar Tracking

## Slide 13: Data: Fixed Solar Panel

## Slide 14: Results

## Slide 15: Conclusion
The solar tracker produced a total of 13.51 more watts than the fixed solar panel over the entire testing window
This confirms that the tracking solar panel will produce more power than the stationary solar panel
Not enough information was recorded to measure the influence of temperature
Better weather conditions are needed for continued testing
This design would need to be extended to a larger scale

## Slide 16: References
How Does Solar Work? (2013). Retrieved October 27, 2020, from https://www.energy.gov/eere/solar/how-does-solar-work
Knier, G. (2008, August 6). How do Photovoltaics Work? Retrieved October 27, 2020, from https://science.nasa.gov/science-news/science-at-nasa/2002/solarcells
Optimum Solar Panel Angle: A Guide: Kuga Commercial Solar News. (2019, September 16). Retrieved October 27, 2020, from https://www.13kuga.com.au/solar-panel-orientation-vs-production/
Solar Panel Efficiency. (2020). Retrieved October 27, 2020, from https://www.solar.com/learn/solar-panel-efficiency/
Solar Performance and Efficiency. (2013, August 20). Retrieved October 27, 2020, from https://www.energy.gov/eere/solar/articles/solar-performance-and-efficiency
Solar Photovoltaic Technology Basics. (2013, August 16). Retrieved October 27, 2020, from https://www.energy.gov/eere/solar/articles/solar-photovoltaic-technology-basics
U.S. Energy Information Administration - EIA - Independent Statistics and Analysis. (2020). Retrieved October 27, 2020, from https://www.eia.gov/energyexplained/us-energy-facts/data-and-statistics.php
https://www.eia.gov/todayinenergy/detail.php?id=45096
https://www.washingtonpost.com/lifestyle/home/considering-getting-solar-panels-here-are-the-right-questions-to-ask/2018/03/09/3190c71a-20c0-11e8-94da-ebf9d112159c_story.html