## Slide 1: Environmental and Economic Life Cycle Assessments of Water Droplet Processing and Traditional Waterjet Cutting Giovanni Guglielmi, Sohani Demian, Jordan Hoffman, Ali Al-Jewad, Nathan Daigle Advisors: Dr. Brad Kinsey, Dr. Weiwei Mo, Benjamin Mitchell Civil and Environmental Engineering, University of New Hampshire, Durham, NH 03824
In 2018, worldwide crude steel production reached 1,809Mt [1]. With metal production and consumption increasing, it is important to note their processes because they have significant global effects on the environment and economy.
Waterjet cutting is a modern form of cleaning or cutting a certain material. This innovative process is used extensively as it poses a reduced environmental threat [2].
Abrasive Waterjet (AWJ) uses a mixture of abrasive particles and a high jet stream of water to cut metal.
Water Droplet Machining (WDM) is conducted on a custom-built waterjet machine that uses high-speed water droplets to cut metal. This process is driven by a Plateau Rayleigh Instability, where a stream of water naturally splits into water droplets after a certain distance traveled [3, 4].
Functional Unit = 100 meters of a 1.15mm thick 316L stainless-steel plate.
Life Cycle Assessment:
  Manufacturing/Assembly Phase
  Operation and Maintenance Phase
  End-of-Life/Disposal Phase
Life Cycle Cost Assessment (LCCA):
  Net Present Value (NPV)
Sensitivity Analyses:
  Abrasive Rate
  Service Life
  Electricity Usage
  Water Rate
Waterjet Systems of Study
Introduction
System Boundary
LCCA Results
Acknowledgements
LCA Results
Abrasive Waterjet (AWJ)
(Left) Exterior of the WDM.
(Right) Model displaying the interior traverse system of the WDM.
(Left) Formation of abrasive slurry before reaching the workpiece.
(Right) Systemic process for AWJ operation.
Sensitivity Analyses
[1] W. S. Assocation, “World Steel Association Home.”
[2] Y. Hu et al., “Mechanism and experimental investigation of ultra high pressure water jet on rubber cutting,” Int. J. Precis. Eng. Manuf., vol. 15, no. 9, pp. 1973–1978, 2014.
[3] B. R. Mitchell, J. C. Klewicki, Y. P. Korkolis, and B. L. Kinsey, “Normal impact force of Rayleigh jets,” Phys. Rev. Fluids, vol. 4, no. 11, pp. 1–23, 2019.
[4] P. Coullet, L. Mahadevan, and C. S. Riera, “Hydrodynamical models for the chaotic dripping faucet,” J. Fluid Mech., vol. 526, pp. 1–17, 2005.
References
Water Droplet Machining (WDM)
Methodology
Perform a comparative life cycle assessment (LCA) on both the AWJ and the WDM.
Perform a life cycle cost assessment (LCCA) on both machines
Conduct sensitivity analyses on key inputs of the machines.
Electricity use and lifetime are the most sensitive WDM parameters analyzed
Abrasive use is the most sensitive AWJ parameters analyzed
A great thank you to Dr. Mo, Dr. Kinsey and Benjamin Mitchell for support in this research along with the U.S. National Science Foundation through award CMMI-1462993.
Impacts | Adjusted Lifetime (+50%) (Years) | Adjusted Water Use (+50%) (L/min) | Adjusted Water Use (-50%) (L/min) | Adjusted Electricity Use (-50%) (kWh) | Adjusted Electricity Use (+50%) (kWh)
GWP | -74.7% | +0.094% | -0.094% | -48.9% | +48.9%
Ozone Depletion | -34.4% | +5.84% | -5.84% | -5.98% | +5.98%
Smog | -1.4% | +0.17% | -0.17% | -48.0% | +48.0%
Acidification | -0.49% | +0.075% | -0.075% | -49.4% | +49.4%
Eutrophication | -17.6% | +1.37% | -1.37% | -23.4% | +23.4%
Carcinogenic | -23.8% | +0.814% | -0.814% | -11.2% | +11.2%
Non-Carcinogenic | -9.63% | +0.58% | -0.58% | -34.8% | +34.8%
Respiratory Effects | -2.98% | +0.23% | -0.23% | -45.5% | +45.5%
Ecotoxicity | -13.3% | +0.75% | -0.75% | -32.2% | +32.2%
Fossil Fuel Depletion | -0.39% | +0.041% | -0.041% | -87.9% | +87.9%
LCCA | -18.37% | +0.97% | -0.97% | -25.65% | +25.65%
Impacts | Adjusted Abrasive Use (-50%) (lb/min) | Adjusted Electricity Use (-50%) (kWh) | Adjusted Electricity Use (+50%) (kWh) | Adjusted Water Use (+50%) (L/min) | Adjusted Water Use (-50%) (L/min) | Adjusted Lifetime (+50%) (Years)
GWP | -38.2% | -24.7% | +24.7% | +0.01% | -0.01% | +0.31%
Ozone Depletion | -74.7% | -0.003% | +0.003% | +0.0078% | -0.0078% | +7.0%
Smog | -75.1% | -6.39% | +6.39% | +0.004% | -0.004% | +0.075%
Acidification | -59.7% | -16.3% | +16.3% | +0.004% | -0.004% | +0.064%
Eutrophication | -74.3% | -2.60% | +2.60% | +0.0073% | -0.0073% | +0.25%
Carcinogenic | -52.3% | -4.16% | +4.16% | +0.027% | -0.027% | +0.83%
Non-Carcinogenic | -78.9% | -3.83% | +3.83% | +0.0084% | -0.0084% | +0.99%
Respiratory Effects | -63.8% | -12.1% | +12.1% | +0.018% | -0.018% | +0.064%
Ecotoxicity | -78.6% | -3.59% | +3.59% | +0.0014% | -0.0014% | +2.7%
Fossil Fuel Depletion | -38.6% | -24.2% | +24.2% | +0.0043% | -0.0043% | +0.18%
LCCA | -33.7% | -16.4% | +16.4% | +2.50% | -2.50% | -21.46%
Objectives
Chart: 
| AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | AWJ | WDM | GWP (kg CO2 eq/100m cut) | Ozone Depletion (kg CFC/100m cut) | Smog (kg O3/100m cut) | Acidification (kg SO2/100m cut) | Eutrophication (kg N/100m cut) | Carcinogenic (CTUh/100m cut) | Non-carcinogenic (CTUh/100m cut) | Respiratory Effects (kg PM2.5/100m cut) | Ecotoxicity (CTUe/100m cut) | Fossil Fuel Depletion (MJ/100m cut)
Manufacturing/Assembly | 0.016342 | 0.18182 | 0.014743 | 0.18182 | 0.015442 | 0.18182 | 0.014542 | 0.18182 | 0.015086 | 0.1773 | 0.017924 | 0.19881 | 0.016399 | 0.17637 | 0.012548 | 0.17391 | 0.015873 | 0.17637 | 0.013129 | 0.18182
Assembly Transportation | 0.016294 | 0.18182 | 0.014813 | 0.18182 | 0.016294 | 0.18182 | 0.016294 | 0.18182 | 0.014445 | 0.1773 | 0.016197 | 0.19881 | 0.014369 | 0.17637 | 0.014369 | 0.17391 | 0.014369 | 0.17637 | 0.014813 | 0.18182
Electricity | 0.050296 | 0.18182 | 0.045723 | 0.18182 | 0.050296 | 0.18182 | 0.050296 | 0.18182 | 0.044588 | 0.1773 | 0.049996 | 0.19881 | 0.044352 | 0.17637 | 0.044352 | 0.17391 | 0.044352 | 0.17637 | 0.045723 | 0.18182
Water | 0.2 | 0.26489 | 0.18182 | 0.26489 | 0.2 | 0.26489 | 0.2 | 0.26489 | 0.1773 | 0.25831 | 0.19881 | 0.28964 | 0.17637 | 0.25695 | 0.17637 | 0.25337 | 0.17637 | 0.25695 | 0.18182 | 0.26489
Abrasive | 0.2 | 0 | 0.18182 | 0 | 0.2 | 0 | 0.2 | 0 | 0.1773 | 0 | 0.19881 | 0 | 0.17637 | 0 | 0.17637 | 0 | 0.17637 | 0 | 0.18182 | 0
Maintenance | 0.2 | 0.0061635 | 0.18182 | 0.0020871 | 0.2 | 0.0038931 | 0.2 | 0.0059813 | 0.1773 | 0.028 | 0.19881 | 0.088724 | 0.17637 | 0.031339 | 0.17637 | 0.016032 | 0.17637 | 0.033257 | 0.18182 | 0.0022361
Disposal | 0.024608 | 0.18182 | 0.035527 | 0.18182 | 0.027897 | 0.18182 | 0.038463 | 0.18182 | 0.014404 | 0.1773 | 0.19881 | 0.022098 | 0.012418 | 0.17637 | 0.031588 | 0.17391 | 0.011354 | 0.17637 | 0.035554 | 0.18182
Chart: Lifetime Costs per 100 meters Cut ($)
| AWJ | WDM
Abrasive | 236.0308 | 0
Water | 10.2085 | 14.8728
Electricity | 98.5548 | 391.9016
Remaining Operation and Maintenance | 21.3391 | 37.4068
Disposal | 0.0074192 | 0.034768
Capital | 26.3249 | 324.1307
WDM has higher costs than the AWJ per every 100 meters of metal cut.
Electricity and abrasives are dominant components in the WDM’s and AWJ’s life cycle costs, respectively.
WDM has higher environmental impacts than the AWJ per every 100 meters of metal cut.
For both waterjets, the operation and maintenance phase is responsible for about 50-60% of the lifetime environmental impacts.
Abrasive Waterjet (AWJ)
Water Droplet Machining (WDM)
Vacuum Chamber
Vacuum Pump
Traverse System
Water Inlet