## Slide 1
HELL GATE WHARF REHABILITATION
Hannah Miller, Samuel Brandt, Cole Contigiani, Adam Wielebinski
Department of Civil and Environmental Engineering, University of New Hampshire, Durham, NH 03284
Location: Bronx, New York on the west side of the East River
Client: Consolidated Edison Company
Usage: electrical substation operations
Site History: built circa 1910; flush truck/waste barge facility
Existing Conditions
Goal: expand site usage & load rating capacity through extension of existing heavy lift area (600psf LL, HL-93 truck load), upgrade of pedestrian area (100-250 psf LL), rehabilitation of sub & superstructure to meet load demands, and fendering system design
Load Rate Analysis
  Pier walls
  Reinforced concrete caissons
  Concrete encased girders
  Existing reinforced concrete deck
  Cast-in-place heavy lift slab
Sea Level Rise Analysis
Deck replacement
  Precast solution
  Precast supplemented with cast-in-place solution
  Cast-in-place solution
Fendering System Design
Cost estimation
Load Rating Analysis
Project Background
Demolition
Cost Analysis
Acknowledgements
The existing deck will be saw cut into sections and removed
Precast Solution
Cast in Place Solution
Scope of Work
Faculty advisor: Dr. Jo Sias
Industry Sponsors: Zack Jenkins
Heavy-Lift Slab
ACI One-way slab analysis based on as-built drawings
Concrete-Encased Girders
RAM Elements used to evaluate sections for applied service strength
Pier Walls & Caissons
RAM Elements used to evaluate compressive strength of pier walls & caissons
Design of 28.75’ channels rated to 600 psf LL and HL-93 AASHTO truck load specification to expand heavy lift area to caisson 2 to pier wall 10
Design of 28.75’ and 33’ channels rated to 250 psf LL to meet client specified non-heavy lift area load requirement
Extend existing heavy-lift slab reinforcement detailing and top of concrete elevation to extents of wharf to meet 600 psf LL from caisson 2 to pier wall 10 and to exceed 250 psf LL capacity in surrounding wharf
Conclusion
From the load rate analysis, the existing heavy lift slab, pier walls, and caissons were determined to have sufficient capacity for the design loads
Options for replacement of the insufficient deck and concrete encased girders includes a full precast solution, a precast combine with cast in place solution, and a full cast in place solution
Based on preliminary cost estimates, the cast-in-place solution is most economical compared to the demolition-precast solution