## Slide 1: Identifying Sources of Heavy Metal Contaminants in Kearny Marsh, NJ Shruti Patel 1, Vincent Favorite 1, Lee Slater 1, Florencia Fahnestock 2 Department of Earth and Environmental Sciences, Rutgers University-Newark 1 Department of Earth Sciences, University of New Hampshire 2
Results
Background (Langan 1999)
Introduction
References
Discussion and Conclusion
We investigated the spatial distribution of contaminants in Kearny Marsh, a freshwater marsh in eastern New Jersey.
Three sites identified as possible pollution sources: 1-E Landfill, Keegan Landfill, and Bibbs Auto Parts.
Sample Collection: April-May 1999.
A grab sampler transferred surficial water samples.
A hand corer collected surficial sediment at 0.5 ft.
Core samples using the Vibracore method were taken at depths of 12, 24, and 36 inches.
Equipment was cleaned between collections.
Sample analysis included TOC, Lead, Arsenic, and Mercury.
Langan Engineering and Environmental Services, Inc., 1999, Sediment and Water Sampling Report: Kearny Marsh, Kearny, New Jersey.
New Jersey Statutory Authority, Surface Water Quality Standards. Section 7:9B. New Jersey Administrative Code, 2016.
No correlation found between mercury concentration and TOC, which means mercury concentrations are not influenced by TOC.
Contamination does appear to be coming from Keegan landfill, but it is not a significant source.
Bibbs Auto Parts appears to be the major contamination source followed by 1-E Landfill.
Comparison with new contamination level data would show if contamination sources changed.
Methods
Contaminant | MCL (PPM)
Mercury | 0.0014
Lead | 0.038
Arsenic | 0.34
Concentration and sample location were processed in QGIS to emphasize spatial relationships between contaminants and possible source location.
Contamination concentrations were compared to NJ government allowable standards.
Lead
Mercury
Arsenic
Figure. 4 All mercury concentrations are above MCL. Highest concentrations near Bibbs Auto Parts.
Figure. 2 All lead concentrations are above MCL. Highest concentrations near Bibbs Auto Parts and 1-E Landfill.
Figure. 3 All arsenic concentrations are above MCL. Highest concentrations near Bibbs Auto Parts, 1-E landfill, and south-east of Keegan Landfill.
Table. 1 Maximum Contamination Limits (PPM) for Mercury, Lead, and Arsenic, respectively.
Total Organic Carbon (TOC)
Figure. 5 Highest concentrations near NJ Turnpike and southeast of Keegan Landfill. Lowest concentrations near Bibbs Auto Parts.
Figure. 1 Highlighted shape and location of Kearny Marsh in New Jersey.
Acknowledgements
CLOSES-GAP 2020 program funded by National Science Foundation (NSF-1801420). Thank you to all CLOSES-GAP team: Ruth Varner, Julice Bryce, Thomas Lippman, Maurice Crawford, Rose Ozbay, and Steve Hale. Also thank you to Emma Burkett and Clarice Perryman for their guidance.
Figure. 6 Image of Kearny Marsh environment. Marsh grasses are roughly 6 ft tall.
Notes: MCL- Maximum contamination limit

## Slide 2
.
Figure. 1 Highlighted shape and location of Kearny Marsh in New Jersey.

## Slide 3
.
Figure. 2 Lead

## Slide 4
.
Figure. 3 Arsenic

## Slide 5
.
Figure. 4 Mercury

## Slide 6
.
Figure. 5 Total Organic Carbon