## Slide 1: Recirculating Water System for Water Droplet Machining Process Connor Buckley, Noah Cleary, Colin Mower, Emily Peacock, and Thomas Splagounias Advisors: Professor Brad Kinsey and Ben Mitchell Mechanical Engineering, University of New Hampshire, Durham, NH 03824
Pressure Release Valve Open
Pressure Release Valve Open
Drain Valve Open
Drain Valve Open
60psi Pump
Drain Valves
Drainage Tank
Traverse System in Vacuum Chamber
R.O. System
Drainage System
Water Droplet Machining (WDM) is a novel manufacturing process comparable to traditional abrasive waterjet machining (AWJ), which uses highly pressurized water to cut a workpiece. AWJ abrasive is financially and environmentally expensive. WDM eliminates the need for abrasive by operating inside a vacuum chamber to eliminate air resistance and produce a concentrated train of water droplets. In WDM, the workpiece moves on a traverse system, while the jet remains stationary. A need for continuous draining is required for steady state operation. Therefore, our task was to create a drainage system that also is used to recirculate and clean the water back through the WDM system.
Design Criteria
CAD Models
Further testing of the R.O. system’s effect on pH.
Recirculate the clean water to the high-pressure pump.
Analyze the amount of heat transferred from the chamber with the insulation installed.
Addition of a dirty water reservoir.
Introduction
Testing Results
Conclusions & Next Steps
Acknowledgements
Completed Recirculation System
System Setup
Testing
Design is within the size limits of 5’x3’x2’
Design is a closed loop that filters and recirculate the water used in the machine
Meets water quality requirements
  pH level: 6.0-8.0
  Silica (SiO2) content < 15 ppm (parts per million)
  TDS (Total Dissolved Solids) level between 50-150 ppm
Suspended solids diameter < 0.2m.
Incorporate a deionization or reverse osmosis system
Recirculation rate: 1 Liter/minute
This work has been performed with mentoring from Ben Mitchell and Professor Brad Kinsey with partial funding from the US National Science Foundation through award CMMI-1462993.
Four different water samples were used in testing. In each testing sample, the water was tested for pH, TDS, temperature, and mass during two-minute intervals.
Vacuum Chamber
Vacuum Pump
Filtration System
Depressurizing Tank
 | Pre-Filtering |  |  | Post Filtering |  | 
Trial # (4 min) | TDS (ppm) | pH | Temp(C°) | TDS (ppm) | pH | Temp(C°)
1 | 230.2 | 9.96 | 10.1 | 37.44 | 10.23 | 20.1
2 | 223 | 9.86 | 16.8 | 29.65 | 10.07 | 18.4
3 | 155.5 | 9.59 | 18.3 | 31.09 | 10.13 | 19.5
4 | 272.9 | 9.79 | 19.9 | 33.03 | 10.19 | 21.3
Workpiece
Liquid pool
Saturated mixture (water vapor + liquid)
Vacuum pump
Superheated water vapor
Reservoir tank
High pressure water pump (60ksi)
Vacuum chamber
Condenser
Filter system
Heat released to ambient air
Low pressure water pumps
Waterjet cutting head
Fan
Drain
tank
T1
T3
T2
T1
T3
T2
Thermocouple