## Slide 1: Sewer Line Evaluation to Improve UNH COVID-19 Monitoring Bailey Jones, Sarah Boisvert, Devon Mexcur Civil & Environmental Engineering, University of New Hampshire, Durham, NH 03824
The UNH Covid Wastewater program surveys biomarkers shed from the SARS-CoV-2 virus using deployable gauze swabs.
Viral biomarkers are strongly correlated to COVID-19 prevalence in the residence halls and provide another level of disease surveillance independent of individual nasal swab testing.
Using this biomarker method, Stoke Hall underrepresents COVID-19 cases compared to the results from the UNH nasal swabs.
Many buildings on campus, including Hubbard Hall, provide reliable data using this biomarker method.
By increasing understanding of UNH sewer networks, the sewer sampling efforts at Stoke Hall may be improved.
Objectives
Background/Motivation
Methodology
Better characterize sewer lines connected to Stoke Hall
Test, optimize, and carry out tracer tests in select sewage lines on campus to confirm flow path, travel time, and mixing
Sites of Interest
Dye Tracer Tests
MATLAB
Visual Tests – Determine pipe connectivity and the amount of time dye remains in the piping system
Camera Tests – Collect time-lapse video of dye in the sewer line to be analyzed using MATLAB
Camera: Afidus ATL-200S (1 Photo / 2 Seconds)
Dye: BRIGHT DYES Dye Tracer Liquid - Red
Hubbard Hall – Control Site
Stoke Hall – Test Site
Site Selection - based on previous capstone project and results from the UNH Covid Wastewater program
Data Conversion: Time Lapse Video  Collection of Images
Image Processing Techniques
Plotting Results
Results
Observations
The results from the Stoke Hall dye-tracer test show the dye moving through the piping system as a plug flow.
The results from the Hubbard Hall dye-tracer test show a greater amount of dispersion than is observed in the results from Stoke Hall.
Higher dye doses require a longer amount of time for the dye to pass through the plumbing in Hubbard Hall as shown by the irregular peaks on the graph. This characteristic of flow is not shared by Stoke Hall.
Special Acknowledgements
Ken Mavrogeorge P.E., City of Dover
Jason Kreil P.E., Woodard & Curran
Adam Moskal P.E., Woodard & Curran
Dr. Paula Mouser
Kellen Sawyer
UNH Facilities/UNH EH&S
Results from the control dye-tracer tests conducted at Hubbard Hall
Graph Information
Two test locations were chosen for the dye-tracer tests at each location, a lower and a higher floor in the building.
The time and volume of red dye added at each location in the building is indicated by black lines on the graphs.
The horizontal axis of the graphs indicates the time since the testing period began in each building.
The vertical axis indicates what percent of the total RGB pixel values was dominated by the R pixel value.
Conclusion
Assuming the SARS-CoV-2 biomarkers acts similarly to dye in the sewer system.
The increased dispersion observed in the piping system in Hubbard Hall results in a greater mixing of the wastewater causing the swabs at this location to encounter a greater percentage of the SARS-CoV-2 biomarkers present in the wastewater than those at Stoke Hall.
Map of Hubbard Hall Sewer Lines
Map of Stoke Hall Sewer Lines
Yellow Tracer-Dye in Sewer
Camera System – Open
Camera System – Deployment Schematic
Results from the dye-tracer tests conducted at Stoke Hall
Camera
System
Suspension
Bracket
Chosen Location
Chosen Location
Camera
Flashlight
Waterproof Case
Sewer