## Slide 1
Design Goals
Architecture & Building Envelope
Renewables
Legacy
References
Environmental Impact
Mechanical Systems
Dynamic Architecture
  Includes classic elements of a New England home while providing suitable mobility and space for the homesteading lifestyle. It includes an open floorplan, split roof design, greenhouse, and root cellar.
  Passive Solar Heat Gain Utilized
  Large windows on the south side take in passive heat, while smaller windows along the north roof release unwanted heat.
Follows ADA standards
By including wheelchair lift, keeping door frames at 36’’, with a 5 ft turning radius, the design is ADA compliant.
Building Envelope
Algae Photobioreactor
Process Flow Diagram
AutoCAD-3D Photobioreactor System Rendering
Summary of Algae Photobioreactor Energy Yield
Photovoltaics (PV)
The 16-kW system will produce 168% of the homes estimated annual power consumption. The system will pay for itself within 12 years.
Project Advisor Felix DeVito
Sunergy Solutions LLC
Department of Energy Solar Decathlon
Passive Greenhouse - Root Cellar Cooperative System
3-ton Ground Source Heat Pump
Energy Recovery Ventilator
Drain Water Heat Recovery + Manual Demand Controls
Solar Assisted Water Heater
Energy Star Appliances
Acknowledgements
U.S. Department of Energy Solar Decathlon
Introduction
Biloria et al. Integrating algae building technology in the built environment: A cost and benefit perspective. Frontiers of Architectural Research, Vol 9, https://doi.org/10.1016/j.foar.2019.12.004.
(ICC), I. C. C. (n.d.). 2018 International Building Code (IBC): ICC Digital Codes. 2018 INTERNATIONAL BUILDING CODE (IBC) | ICC DIGITAL CODES. Retrieved April 14, 2022, from https://codes.iccsafe.org/content/IBC2018
Author(s) International Code Council. (n.d.). Climate zone map from IECC 2021. Climate Zone Map from IECC 2021 | Building America Solution Center. Retrieved April 14, 2022, from https://basc.pnnl.gov/images/climate-zone-map-iecc-2021
“U.S. Access Board.” ADA Accessibility Standards (Enhanced Single File Version), https://www.access-board.gov/ada/.
University of New Hampshire, Departments of Civil, Environmental, & Mechanical Engineering
Jacob Roberts, Nathan Raffa, Will Baldwin, Wilder Byrne, Cole Gorham, Ben Guertin, Elizabeth Gunn, Miles Libby
The Green Standard Team
Average Algae Energy Density​​​​ (kWh/kg)​​ | Energy Yield ​​ (kWh/day)​​ | Net Balance ​​ (Production – Consumption) ​​ (kWh/day)​​ | Net Generation​​ (kWh/year)​​
7.5 | 6.83​​ | 4.43​​ | 1,551​​
Objective
The Green Standard will contribute to environmentally conscious, self-reliant and homesteading lifestyles with our residential design. The team presented this design in the 2022 DOE Solar Decathlon Design Challenge.
Solar Decathlon
An annual collegiate competition where teams around the world take up the challenge to design highly efficient, innovative, low-carbon buildings powered by renewable energy. Each team is judged based on 10 contests.
Homesteading
Lifestyle of self-sufficiency where gardening and raising livestock on one’s property is common. There is a current resurgence of this sustainable lifestyle.
Modern Homesteading
Integrating historical, New England homesteading practices with modern, cutting-edge engineering and technology.
New Hampshire Location
Function in accordance with all aspects of New England’s environment, climate, and lifestyle.
Net Zero
A home where the annual amount of energy used is met or exceeded by onsite generation.
Chart: 
Total Savings | 123884
Cost of Utility Usage | 36900
Net Savings | 84220
$84,220
$39,664
$123,884
US Dollars
25 Year Analysis of PV Savings
Chart: Water Usage Reduction
| Irrigation | Appliances | Fixtures | Total
Average Household | 14618.4 | 8030 | 32558 | 55206.4
The Green Standard | 2684.4 | 4050 | 17477.75 | 24212.15
Graywater System
Chart: Annual Home Energy Consumption vs Generation
| kWh
Annual Home Consumption | 7353
#REF! | 1
Solar Photovoltaics Generation | 19739
Algae Biofuel Generation | 1551
538 Greenfield Road, Peterborough NH
Climate Zone 5A
Zoned Residential
Outside of Public Water and Sewer Zones
Within 5 Miles of Hospitals, Schools, Grocery, Downtown Amenities, and Recycling center
12.2 Acres
The Green Standard presented our project to the CEE 719 - Green Building Design class with the intention of passing on valuable insight to future Capstone teams.
Roof: R-67.6
Wall: R-46
Floor: R-35
Foundation: R-49
Architecture
Engineering
Market Analysis
Durability and Resilience
Embodied Environmental Impact
Integrated Performance
Occupant Experience
Comfort & Environmental Quality
Energy Performance
Presentation
Algae + Nutrients + CO2
Feeding Tank
Pump
Algae Photobioreactor
Filter
Recirculating Growth Medium
Filtered Biomass
Algae PBR
Algae
Drying
Filtered Biomass
Dried Biomass
Pelletization via Compression
Combustion
Greenhouse
Root Cellar
Basement
First Floor
Second Floor
31,000 GPY Reduction
-46.3%
-56.1%
-81.6%
Improves self-sufficiency​
Respired CO2 piped to greenhouse for plant photosynthesis
Recycles water for greenhouse & garden use​
Reduces load on septic system
Drain Water Heat Recovery
Highly Efficient Low-Carbon Heating and Cooling
Notes: Top banner: US Dep. Of Energy Solar Decathlon, team name, members,
HOMESTEADING , NET ZERO
Build this around homesteading, we chose these materials or this architecture for this reason relating to homesteading