## Slide 1: PFAS IN VERMONT BACKGROUND SOILS Lindsay Guertin (PM), Callie Beard, Maeve Richardson Advisor: Paula Mouser Sponsor: Harrison Roakes, Sanborn Head College of Engineering and Physical Sciences, University of New Hampshire, Durham, NH 03824
Vermont Sampling
Sampling and Analysis Plan (SAP)
Acknowledgements
Figure 4. 95% Upper Prediction Limits
(1) U.S. Environmental Protection Agency (EPA). (2021). Statistical Software ProUCL 5.1.00 for Environmental Applications for Data Sets with and without Nondetect Observations. https://www.epa.gov/land-research/proucl-software#about
(2) Singh, A. & Maichle, R. (2015). ProUCL Version 5.1.002 User Guide. U.S. EPA. https://www.epa.gov/sites/default/files/2016-05/documents/proucl_5.1_user-guide.pdf
References
Statistical Approach - ProUCL
Alpha Analytical
Morghan Carr, Department of Civil and Environmental Engineering
University of Vermont
Figure 5. Upper Tolerance Limits
SAP
Statistical Analysis
Results: BTVs
Recommendations
VT Sampling
Slight downward trend as chain length increased
Even chained compounds had significantly higher concentrations than odd chained compounds (Figures 4 and 5)
Few outliers caused highly skewed data
Recommendations:
UPL or UTL values without outliers should be used as the BTVs as they both account for most of the data, representing the lower distribution of background concentrations
Neither UPL or UTL is the best but the UTL accounts for slightly more of the data
Focus should be on compounds with prior knowledge and established regulations to help create rules and regulations for background levels
Recommendations/ Trends
ProUCL was developed by EPA to analyze environmental data sets
Can analyze data with and without detected concentrations
Rosner’s Test used to determine outliers
Conducts test to determine which distribution the data best fits
Figure 2. Outlier test used to determine the outliers present in the data.
Figure 3. BTV test used to analyze the data with non-detected values.
Figure 1. Sample input of data into ProUCL.
Outlined PFAS sampling guidelines, sampling locations, an analyte list, and analytical procedures
Guidelines were created that detailed sites that should and should not be sampled based on known PFAS sources
Described proper precautions that need to be taken when sampling for PFAS
Preferred Sites: Forests, Parks, Easily Accessible Sites
Potential Point Sources: Fire Stations, Airports, Wastewater Treatment Facilities, Biosolids, and Hazardous/Solid Waste Facilities
Motivation
Need to define background levels for rules and regulations regarding PFAS
Increasing demand for information on these compounds
Increasing concerns regarding the impacts of PFAS on the health of humans and the environment