## Slide 1
High-Frequency Data Reveal Patterns of Dissolved Organic Matter Production
and Nitrate Removal Within a Low-Head Coastal Reservoir – B51M-2417
Christopher Whitney*, Wilfred Wollheim
University of New Hampshire, Department of Natural Resources and the Environment
*chris.whitney@unh.edu
Background
Sensor Calibrations Vary by Instrument and Matrix
Study Area & Methods
Conclusions
Dissolved organic matter (DOM) is often the primary form of dissolved organic carbon (DOC) and nitrogen (DON) in aquatic ecosystems while nitrate (NO3) is the primary form of inorganic nitrogen, usually associated with human activity
Impoundments receive large amounts of DOM where it can be stored, transformed, and exported downstream
Fluorescent and ultraviolet in situ sensors can quantify concentrations of DOC, DON, and NO3 with reasonable accuracy
High-frequency mass balances of DOC, DON, and NO3 can provide information on dominant biogeochemical processes taking place in impoundments
In situ sensors can be used successfully to estimate input-output mass balances of DOC, DON, and NO3 in fluvial systems
High-frequency DOC, DON, and NO3 mass balances help determine the timing of when shifts in biogeochemical processing occurs
However, in situ sensors are susceptible to many different types of failure
Acknowledgements
Plum Island Ecosystems LTER (OCE–1238281 and 1637630)
EPA STAR Graduate Research Fellowship (FP-917819)
Reservoirs Alter Downstream C:N Fluxes
Study takes place in the reservoir created by the South Middleton Dam on the Ipswich River in Middleton, MA
Paired SUNA NO3 sensors and Turner C3 Fluorometers were deployed at the input and output of the reservoir
Fluorescent dissolved organic matter (fDOM) from Turners converted to DOC and DON via grab samples
Removal of catchment-area weighted DOC, DON, and NO3 calculated as:
High-frequency mass balances of DOC, DON and NO3 determined via in situ sensors can tell us when water bodies shift from removal to production of organic carbon, organic nitrogen and NO3, suggesting changes in dominant biogeochemical processes and processing rates
Datalogger
Wiper
6/17/19
6/30/19
Shift from DOC removal to DOC production occurred on 6/30/19
Shift from DON removal to DON production occurred roughly 2 weeks earlier on 6/17/19
SUNA at reservoir inflow plagued with issues resulting in missing data:
  Campbell Datalogger failure from 5/8/19 to 8/1/19
  SUNA wiper failure from 8/1/19 to 8/22/19
  SUNA lamp failure on 10/5/19
However, NO3 mass balance indicates removal during deployment period when data were collected and logged
NO3 data from previous years show a shift to substantial NO3 removal during a similar time period
Lamp
DOC:
Input:
r2 = 0.53, p = 0.1
Output:
r2 = 0.86, p = 0.01
DON:
Input:
r2 = 0.63, p = 0.07
Output:
r2 = 0.76, p = 0.03
NO3:
Input:
r2 = NA, p = NA
Output:
r2 = 0.95, p < 0.01
Input DOC:DON was relatively stable over the deployment period
Output DOC:DON indicates the reservoir consumed more DOC relative to DON