## Slide 1
Li-Poly Battery
RC
Receiver
Telemetry Radio
Power Module
GPS
Motor
I/O
Design:
Intel RealSense Depth Camera and Jetson Nano Companion Computer communicate with Pixhawk4 Flight Controller
3DVFH* Algorithm equipped for autonomous obstacle detection during flight
Coordinate flight paths and avoid collisions with obstacles
Future Considerations:
Support avoidance of moving obstacles
Propeller Guard
Bi-Propeller
Pixhawk
920 KV DC Brushless Motor
915 MHz Telemetry Radio
6000 mAh 11.1V Li-Poly Battery
2.4 GHz RC Receiver
Weatherproofing
Quadcopter Fleet
Quad-X Swarm
Autonomous Quadcopter Fleet
Propeller Guards
Obstacle Avoidance
Diagnostics
Autonomous Flying
Autonomy · Durability · Multi-Communication · Reliability · Safety · Versatility
The UNH Quad-X Swarm is an interdisciplinary group comprised of students from the Advanced Controls Lab, who specialize in the disciplines of Mechanical Engineering and Computer Science. The team is dedicated to the design and deployment of an autonomous fleet of quadcopters equipped with real-time obstacle detection, path planning, and GPS communication. ​Quad-X aims to improve quadcopter robustness in turbulent weather conditions while carrying out safe and efficient autonomous missions. With the inclusion of a diagnostic panel, obstacle detection, and SolidWorks simulations, the team seeks to implement seamless autonomous flights in a variety of SWARM applications. With a strong focus on innovation, creativity, and teamwork, the UNH Quad-X Swarm team is poised to make a significant impact in the field of autonomous robotics and quadcopter technology while revolutionizing how we explore, observe, and interact with our world.
Introduction
Grant Arnold1, Jacob DeSousa2, Alison Kim, Dan Maille2
Christian Baduria, Preston Collette, Yicheng Su
Dr. May-Win Thein, Ph.D.
1Project Manager, 2Financial Officer
University of New Hampshire
Department of Mechanical Engineering & Department of Computer Science
Electronics & Software
Multi-Quad Path-Planned Mission: Aerial View
Courtesy of Masters Student
Debarpan Bhowmick
Kingman Farm,
Durham New Hampshire
1720 KV DC Brushless Motor
Tri-Propeller
GPS
Occipital Structure Core Camera
UP Core Companion Computer
Carbon Fiber Frame
Optical Flow and Distance Sensor
Wi-Fi Module
Gazebo Flight in a Simulated Forest
Experimental Internal Temperature Response of Electronics
QGroundControl Mission Planner
Path-Planning
Weatherproof Housing
5V Cooling Fan
Ventilation Design V 1.2.0
Initial Design
V 1.1.0
Internal Cooling Fan Design V 1.3.0
Lidar Ground Surveying
Obstacle Detection & Avoidance
Specifications:
Map areas of land above the forest canopy to identify obstacles
Quadcopters navigate under the tree canopy equipped via pre-defined paths
Software implemented using python code
Connected via SSH and local network
Security
Snow Depth Detection
Space Exploration
Terrain Mapping
Unexploded Ordinance Detection
Wireless Communication
Infrastructure Inspection
Real-Time Obstacle Detection
Search and Rescue
SWARM Applications:
Initial Design Iterations
Design Criteria:
Propeller Protection During Flight
Sturdy and Lightweight Design Optimization in SolidWorks 2021
Motor Mounting Integration
Withstand an Impact ~30N
Von Mises Stress Result
Displacement Result
Max: 58.7 MPa
Max: 19.81 MPa
Max: 6.5 mm
Max: 68.5 mm
SolidWorks 2021 Optimized Simulations
V1.0.0
V4.0.0
Von Mises Stress Result
Displacement Result
Fatigue Failure Plot of PLA+
Collision Impact Equations:
Functionality:
Monitor real-time flight information, battery health, and flight duration
Improved existing GUI using HTML & JavaScript framework with Python code
Real-time updates give simultaneous access to important diagnostic information for each quadcopter
SSH into quads to arm and launch missions with a single button
ESC
Motor
Internal CPU
PX4 Vision
X500 Quadcopter
References
[1] Obstacle Avoidance for Drones by 3DVFH* Algorithm by Tanja Baumann
[2] Multicopter PID Tuning Guide. Multicopter PID Tuning Guide | PX4 User Guide. (2021, June 3). Retrieved February 6, 2023
[3] Holybro Pixhawk 6C. Holybro Pixhawk 6C | PX4 User Guide. (2023, March 23)
Acknowledgments
With utmost gratitude, we thank the generous assistance of the UNH Parents Council Committee towards our pursuits. We extend our sincere appreciation to our graduate students: ChanLing Beswick, Debarpan Bhowmick, Patrick Close, Tom Fuller, Chris Hashem, Jacob Shaker, and Andrew Weeks, for their invaluable expertise and knowledge throughout the year. A heartfelt thank you goes to Dr. May-Win Thein, our project mentor and advisor, for your dedication to our education and your willingness to go above and beyond to ensure our success in the field of engineering and professional lives.
Intel RealSense Depth Camera & Sensor
NVIDIA Jetson Nano
MavLink
Pixhawk
Camera
ROS
Transmitter
Motor I/O
Ground Station
PID Control
Software
Internal Electronics
Power
Sensors
Lidar
Momentum equation:
Newton’s Second Law:
Acceleration=
Table of Assumptions | 
UAV Initial Velocity | 6.5 m/s
UAV Final Velocity | 0 m/s
UAV Mass | 2.086 kg
Time of impact | 0.5 sec
Satellite
Real-Time Diagnostic Panel
Design Criteria:
All-Weather Electronics Protection
Efficient Component Layout and Compact Design
Internal Fan for Temperature Regulation
Future Considerations:
External USB-C Accessibility
Housing Model | , 63.2% Method | Resulting 1st Order Transfer Function
Fully Enclosed Model | 1124 sec | 
Ventilation Design | 1217 sec | 
Internal Cooling Fan Model | 687 sec | 
Housing Model |  | Resulting 1st Order Transfer Function
Fully Enclosed Model | 1124 sec | 
Ventilation Design | 1217 sec | 
Internal Cooling Fan Model | 687 sec | 
Mechanical Engineering:
Computer Science:
Faculty Advisor: