## Slide 1: UNH BAJA RACING 2024 Department of Mechanical Engineering, University of New Hampshire Henry Gorhan, Geoff Smith, Justin Paul, Nate Huckins, Aidan Palermo, Bobby Putnam
Senior design project focused on the development, and fabrication of an off-road 4WD vehicle to compete in the Baja SAE competition. Baja SAE is an intercollegiate design competition organized by the Society of Automotive Engineers (SAE). The vehicle must be capable of withstanding the rigors of rough terrain while maintaining speed, agility, and durability.
Students utilized the entire array of skills gained in Mechanical Engineering degree. This included extensive use of Machine Design, CAD/FEA, Material Science, and Manufacturing.
Frame
Specifications
Front Suspension is Designed to Minimize Bump Steer and Camber Change.
Minimize Sprung Weight by Utilizing Billet Aluminum & Designing Custom Knuckles.
Design to Lower Instant Centers of Mass & Reduce Forces in Control Arms by Utilizing a Reverse Engineered Tall Knuckle Assembly.
Improvements
Achieved Desirable Trailing-Arm Suspension Kinematics.
Maximized Front and Rear Suspension Travel (Increase Droop) Via Complex Bend Geometry while Maintaining Compatibility with Off the Shelf Components.
Utilized Smaller Diameter Chromoly Trailing Arms, Connecting Links & Front Control Arms to Reduce Sprung Weight while Maximizing Strength.
Specifications
Hydraulic Braking to all Four Wheels
Dual Kill Switch (One by Driver one by Engine)
Fully Mechanical Steering
Brake and Reverse Lights
Electronic Switch for activating Four Wheel Drive
Improvements
Custom Brake Rotor Design
Decreased Vibration with Engine Bushings
Project Overview
Powertrain
Acknowledgements
Specifications
Engine: Kohler CH440 14 HP
Transmission: Gaged Engineering GX9 CVT with 3.9-0.9 gear range.
DANA H12 final drive transaxle – 13.25:1 ratio
4x4 transfer case
Improvements
Transaxle selection yielded a 50% weight reduction in comparison to previous design.
CVT tuned to minimize belt slipping and increase final drive ratio.
Reduced U-Joint use to decrease mechanical loss
Improved compatibility for future use.
Collaborated with industry partners for highly specialized manufacturing.
Suspension and Handling
Specifications
1020 AISI Steel Frame with Roll Cage to Surround and Protect Driver.
Subframe and Mounting Assemblies to Support, Integrate, and Package Subsystems.
Improvements
Improvements
Established Pipe Bending and Notching Process for Rapid Fabrication and Improved Strength by Reducing Welds and Minimizing Open Ended Pipes.
17% Reduction in Weight (150lbs -> 125lbs)
Advisor: Ivaylo Nedyalkov
CEPS TSC: Noah MacAdam, Scott Campbell, Kevan Carpenter, Sheldon Parent, CEPS Makerspace
CEPS ME Department: Kelly Danforth, Shannon Silver, Nathaniel Burnich
Sponsors: SAE International, Sig Sauer, Turbocam International, Todd Gross, SolidWorks Corp., Kohler, Fox Factory Inc., Individual Donors
Engine Performance: Kohler CH440
Frame Manufacturing
Developed a Process to Maximize Tubing bends instead of Welding to Maximize Strength, Minimize Weight, and Enhance Aesthetics.
Powertrain & Suspension Compatibility
Powertrain and Suspension Designed to Remain Compatible with Polaris Differential & other off-The-Shelf Parts.
Continuously Variable Transmission
Gaged Engineering CVT Allows for “Infinite” Gear Ratios Without the need of a Gearbox
Custom Front Suspension
UNH BAJA Knuckle Assembly Reverse Engineered From Can-Am Maverick R Tall Knuckle Design
Manufacturing & Design
Utilized Tig Welding (GTAW) for Fabrication of the Frame, Roll Cage & Suspension Components.
Hydraulic Pipe Bender is Required for Desired Frame Geometry.
Custom Drivetrain Components with Complex Features Required the Use of Laser Scanning (Reverse Engineering) and Wire EDM Machining.
Engine RPM
Theoretical Speed
(mph)
Torque (ft-lb)
Engine RPM
Power (HP)
Controls