## Slide 1: Bow Elementary School Expansion Ian Sargent, Joe Payson, Christian Sommers, Ben Towler Department of Civil & Environmental Engineering, University of New Hampshire, Durham, NH 03824
Bow Elementary School (BES) is located at 22 Bow Center Road, Bow, New Hampshire. Built in 1978 with a recent addition erected in 1991, the existing school spans around 57,000 square feet.
With the population of Bow increasing by around 9.4% from 2010 to 2021, the current school can no longer house all the incoming students.
For a solution, the H.L. Turner Group proposed a 12,200 square foot addition including two stories (4 classrooms on each floor) and a partial basement.
With this information, the team has decided to provide an alternative building design for the H.L. Turner Group.
Project Deliverables
Steel Framing Design
Introduction
Sustainability Options
Cost Estimation
Acknowledgements
Energy Efficient Windows
LED Lighting
Solar Panel Array
Roof-Top Garden
CMU Wall Design
Foundation Design
ACI Committee 318-19, & American Concrete Institute. (2019). Building code requirements for structural concrete (ACI 318-19). American Concrete Institute.
American Institute Of Steel Construction. (2015). Steel construction manual. American Institute Of Steel Construction.
Masonry Society (U.S, & Masonry Society (U.S.). TMS 402/602 Committee. (2016). Building Code Requirements and Specification for Masonry Structures. The Masonry Society.
Structural Engineering Institute (2010). Minimum Design Loads for Buildings and Other Structures. American Society of Civil Engineers.
References
For this project, the team had their sights set on providing the following deliverables:
Site Planning and Design
Steel Framing Plan
CMU Wall Design
Foundation Design
Sustainability Options
Foundation Design
Soil unit weight of 127.32 pcf 20 (20)
Peak friction angle = 40°
Zone of influence = 8’ below proposed foundation
Bearing Capacity:
2’ strip footing below all load bearing CMU walls
Set at elevation of 455’ MSL NGVD (7’ depth)
Reinforced with #8 rebar at 1” horizontal spacing
Four vertical rebar rows, spaced 2.5 inches apart, with the lowest at 81.75 inches
, normal weight concrete
Soil Investigation
We would like to thank our sponsors, Bill Hickey and Paige Wilber, from the H.L Turner group. We also appreciate all the help and guidance from our project advisors Dr. Bell and Dr. Kalmogo.
Site Design
Critical Wall: North Wall Elevation
Demands
Roof total dead weight of 24psf includes:
Steel Member Selection
Classroom Joist: 16K2
Corridor Joist: 10K1
Joist Girders: 24G7N10.2K
Floor Deck: 1.5VL20
Roof Deck: 1.5B20
Chart: Corrected SPT Blow Counts Vs. Elevation
| 24 | 6.75 | 2.25 | 49.5
B1 | 461 | 459 | 457 | 451
B2 | 456 | 454 | 452 | 448.5
B3 | 457 | 455 | 453 | 450
Existing Conditions
Proposed Development
Grading
Regraded proposed roadway and surrounding landscape
Directs water away from building to reduce flood risk
EPDM
Insulation
Lighting
MEP/FP/AV
Solar panels
Steel deck
Floor total dead weight of 63.1psf includes:
Linoleum
Lighting
MEP/FP/AV
Deck
Concrete Slab
Floor Live Load:40psf
Snow Load: 50psf
Wind Load: 16.4psf
Seismic Load: Not Considered
South Wall Construction View
Largest Embedment Depth (7’) -
Smallest Embedment Depth (2’) -
Section View of North Wall
$145,000
Reduces amount of energy required for heating by 12%.
$167,800
Saves up to 25% on total electricity bill.
$822,000
Potentially generates an additional 7900 kWh/year.
$694,500
Creates additional insulation for roof and promotes sustainable thinking.
Drainage
Existing building not included in design
Drainpipe and water storage dynamically sized based on 24 hour, 50-year precipitation
Prevents overtopping of water storage onto athletic field
Specifications
8” x 8” x 16” Fully Grouted CMU Block
Mortar Type S
Normal Weight = 125pcf
Grade 60 #5 rebars @ 48” O.C.
Second Floor Framing Plan
North Wall Construction View