## Slide 1
Powertrain
Frame
Sponsors
Brake Assembly
  6061-T6 Aluminum components withstand 2000N (450 lb-f) force from the driver.
  Vertically mounted master cylinders optimize packaging, braking force, and pedal travel.
  Wilwood Brake Calipers
  Track Brake pads
Safety Considerations
  6-point RaceQuip harness holds driver securely in place.
  Driver must be within the rollover protection envelope.
  Impact attenuator on the front of the car absorbs impact forces.
Steering Column
  Utilizes double universal joint designed for automotive steering shafts
  Rack mounted behind the front axle to improve Ackermann Steering..
Controls
College of Engineering and Physical Sciences
Mechanical Engineering Department
Team Members
Project Managers: Mathieu Champagne, Trevor Legros
Controls: Ryan Gervais, Owen Pratt
Frame: Mathieu Champagne, Todd Brown
Powertrain: Trevor Legros, Sam Osgood
Suspension: Ryan Gervais, Owen Pratt
Faculty Advisor: Juan Carlos Cuevas Bautista
Purpose
  Resist chassis roll – maximize tire contact patch with road
  Roll center placement prioritizing responsiveness
  Minimize roll center migration, increase stability/predictability
  Select coilover to achieve desired ride frequency and roll rate
  Adjustability: static camber, ride height, toe angle
Geometry Selection
  Double wishbone, Short-Long Arm (SLA), pushrod actuated
  Rear bell-crank repositioned out-of-plane to improve packaging
Component Modeling & FEA
  SolidWorks 3D modeling - FEA and kinematics in MSC Marc Mentat, MATLAB, & LOTUS Shark
  Calspan tire data used to predict dynamic forces
Manufacturing
  Waterjet in Olson Center, finish machining in CEPS machine shop, TIG welding
Suspension
UNH Precision Racing Team 2024
Engine
  2016 KTM 450 SX-F
  Max Torque : 34lb-ft @ 7000 RPM
  Max Power: 53 HP @ 9500 RPM
  Naturally aspirated, 100 Octane
  High torque at low RPM's and linear power curve makes driving easier for inexperienced drivers
Drivetrain
  Chain Drive
  Drexler Limited Slip Differential
  RCV Half-Shafts
  Aluminum differential designed to allow tightening of the chain using an eccentric disk concept, various locking points.
Intake Manifold
  3000 cc plenum
  Utilize AT Power's FSAE throttle body with built in restriction diameter
  Made from printed titanium, experimenting with ABS plastic printing.
  Runner length of 264 mm with a single 42 lb./hr. injector firing directly at the intake valves.
Design Goals
  Torsional stiffness greater than 1500 [Nm/deg]
  Maintain weight less than 100 lbs
  Effectively maximize space for the driver, powertrain, suspension, and controls
  Meet all structural qualifications outlined by the SAE structural equivalency survey
Current design
  TIG welded AISI 1020 steel tube members
  Torsional stiffness equal to 1,831 [Nm/deg]
  Weight of manufactured frame equal to 89lbs
  Allows for optimal suspension attachment
  Fits a driver of the 95th percentile
  Adheres to SAE rules to ensure driver safety
  Torsional stiffness test for simulation validation
New design
  Main goal of weight reduction
  Efficient use of space
  Increase engine bay volume
  Shifted driver position
  Increased manufacturability
  Weight reduction of 10 lbs
Abstract
UNH PRECISION RACING IS A STUDENT-PROJECT ORGANIZATION DEDICATED TO FOSTERING THE DEVELOPMENT OF YOUNG ENGINEERS THROUGH THE FORMULA SAE (FSAE) COMPETITION SERIES. THE FSAE PROGRAM EXPOSES STUDENTS TO ENGINEERING OUTSIDE THE CLASSROOM, INCLUDING DESIGNING, MANUFACTURING, PROJECT MANAGING, AND COMMUNICATING WITH THE WIDER COMMUNITY
Special Thanks to the UNH Alumni Association and UNH Dean's Allocation
Todd Gross