## Slide 1: Optimization of Anchoring Isonicotinic acid on TiO2 NP for Applications in Dye Sensitized Photocatalysis Phoebe Nitchals, Matthew Huebner, Charles Wilson, Christine A. Caputo* Department of Chemistry, University of New Hampshire, Durham, NH 03824
Though Dye Sensitized Photocatalysis (DSP) is a rapidly expanding field of research in green chemistry, its applications are limited, which is in part due to the cost-prohibitive nature of the methods currently available. The complex synthetic schemes require skilled chemists and a significant time investment to synthesize, characterize and isolate the catalysts used.
To simplify the process, and decrease costs, we propose to test if pre-anchoring of the axial ligand of a H2 generating catalyst to TiO2 will allow catalyst self-assembly on the surface.
Experimental
The pre-anchoring of Isonicotinic acid to TiO2 and allowing Co(dmg)2Cl2 to self-anchor is effective and is a significantly cheaper alternative to anchoring a pre-assembled of Co(dmg)2(ISO)Cl. This method decreases the total material cost to produce a micromole of hydrogen gas 400-fold.
Green energy will continue to be an unsolved problem if it cannot become affordable. This work demonstrates a creative strategy to minimize costs while maintaining the similar efficiency.
Introduction
Cost Analysis
Conclusions
Acknowledgements
Results
Characterization Methods
References
I am incredibly grateful for those who guided me along this process particularly Cj Wilson, Christine Caputo, and Matthew Huebner. I could not have done this without their support and wisdom.
Lakadamyali, F.; Reynal, A.; Kato, M.; Durrant, J. R.; Reisner, E. Electron Transfer in Dye-Sensitised Semiconductors Modified with Molecular Cobalt Catalysts: Photoreduction of Aqueous Protons. Chemistry: A European Journal 2012, 18, 15464–15475.
Lakadamyali, F.; Kato, M.; Muresan, N. M.; Reisner, E. Selective Reduction of Aqueous Protons to Hydrogen with a Synthetic Cobaloxime Catalyst in the Presence of Atmospheric Oxygen. Angewandte Chemie 2012, 124, 9515–9518.
Lakadamyali, F.; Reisner, E. Photocatalytic H2 Evolution from Neutral Water with a Molecular Cobalt Catalyst on a Dye-Sensitised TiO2 Nanoparticle. Chemical Communications 2011, 47, 1695.
This technique is used to examine the morphology of TiO2. The original structure is mesoporous and should not be altered by loading ISO to the surface.
These images confirm preservation of TiO2 morphology when TiO2 is loaded with [2.5mM] ISO conditions.
ATR-FTIR is used to ensure that ISO is loaded onto the surface.
Peak at 1408cm-1 is the symmetric stretching peak of a CO double bond. Peak at 1550cm-1 is asymmetric stretching of the CO double bond and confirms ISO loading
This data is used to assess the crystal structure of the loaded TiO2 to blank TiO2 .
The mixture of TiO2 used is a unique ratio of rutile and anatase phase titanium called P25.
This confirms that loading the ISO does not alter the crystallinity of the TiO2 nanoparticles.
Isonicotinic Acid
Titanium Dioxide
Cobalt Precursor
Phosphonic Acid
Improved Self-Assembly Procedure
Literature Self-Assembly Procedure
Ethanol
Methanol
Stir 30min
Wash pellet
Add catalyst precursor
Stir 5min
40˚ C for 1hr
Slowly precipitate
Wash
Mix with TiO2
Literature
Optimized
Scanned from 10-60 2ϴ (°) at 1.5 °/min
10 µm
1 µm
Research Questions
Can we optimize iso-nicotinic acid (ISO) loading to maximize catalyst self-assembly on TiO2?
Is this method a significantly cheaper alternative to anchoring a pre-assembled cobaloxime (Co(dmg)2(ISO)Cl)?
10 µm
1 µm
1 µm
10 µm
Blank TiO2
ISO@TiO2
TiO2 NP
Surface
CoP@TiO2
CoISO@TiO2
Isonicotinic Acid
Phosphonic Acid