## Slide 1: Low-Cost LiDAR Lens Autofocus System for Cinema Cameras Nolan K. Juneau (nkj1006@usnh.edu) Faculty Advisor: Dr. Richard Messner, Ph.D Department of Electrical and Computer Engineering, University of New Hampshire
Software Design
References
TFMini-Plus Arduino Library for the Benewake TFMini-Plus LiDAR Sensor https://github.com/budryerson/TFMini-Plus
LiquidCrystal_I2C Arduino Library for I2C LCD Displays
https://github.com/johnrickman/LiquidCrystal_I2C
AccelStepper Arduino Library for Stepper Motors with Acceleration/Deceleration Support
https://github.com/waspinator/AccelStepper
Tenney, Matthew. “Microsoft Kinect – Hardware.” Geospatial Modeling & Visualization, Geospatial Modeling & Visualization, 5 July 2012, https://gmv.cast.uark.edu/scanning/hardware/microsoft-kinect-resourceshardware/
Goal: Design and build a functional, low-cost autofocusing system for cinema cameras using inexpensive LiDAR technology that can be adapted to any cinema camera rig.
Motivation: Professional cinema cameras (unlike many consumer cameras) do not have in-built autofocusing, requiring a dedicated camera crew member to manually “pull focus”. LiDAR-based autofocus systems do exist but are prohibitively expensive for independent filmmakers. Consumer microcontroller/electronics hardware and 3D-printing technology can achieve similar performance for a fraction of the cost.
Requirements:
Allows for autofocus capability for all lenses with a manual focus ring
Designed as a mountable, self-contained unit with user control:
  Main case should be no larger than 150mm x 150mm x 75mm
Be powered entirely by 5V USB power for ease of portability
Total material cost of the system should not exceed $100
Arduino NANO
Microcontroller
+5V
USB
Power
A4988 Stepper Motor Driver
+12V
Barrel
Jack
Power
TF-Luna
LiDAR
Sensor
Stepper Motor
Circuit Design & Block Diagram
Future Advancements
Distance Sensor: TF-Luna LiDAR Sensor:
  Single-beam distance detection, maximum range of 9m (29.53ft)
  Connected to Arduino Nano via Serial protocol
  Mounted to camera via 3D-printed mount to ¼-20 screw thread
Microcontroller: Arduino NANO
Stepper Motor: NEMA-17 (17HS08-1004S) with 5-1 gear reduction:
  Controlled via A4988 stepper motor driver board
  600mA current input requires separate 12VDC power supply, achieved via USB to 12V barrel jack step-up cable (center-positive)
3D-printed case designed in SolidWorks:
  Measures 5.12”W x 3.15”L x 1.97”H
4x20 LCD display for GUI & live distance feed (using I2C protocol):
  Three push-buttons for GUI control
Two 4-pin Molex connectors to connect motor and LiDAR sensor
Curve extrapolation algorithm can be smoothed for more accurate, “natural” focusing
Increase single-beam distance for use with telephoto lenses
Single-beam LiDAR is limiting, can be expanded using LiDAR arrays:
  Incorporate face/body tracking and selective subject focusing via image processing
  Microsoft Kinect LiDAR arrays are easily sourced and highly capable for motion tracking
LCD
Screen
Push Buttons
Introduction
Results
Hardware Design
Programmed via ArduinoIDE in C++ (~700 lines total)
“Calibration sequence” determines focus curve for any given lens:
  Sets motor position for focus at four distances (0.6m, 1m, 3m, & infinity) and extrapolates focus “curve”
Stores three “focus calibration profiles” via Arduino’s internal nonvolatile EEPROM memory
Reset function clears all saved EEPROM calibration data
Effectively keeps subjects in focus for wide/medium lens focal lengths (<50mm):
  Maximum Range of 9m (29.53ft)
Three “calibration profiles” means settings are saved for multiple lens/camera setups, even when powered off
Subject
Distance
Distance
Data
(Serial)
I2C
Screen
Data
Focus Ring Control
Electronics can be simplified to a single PCB using an STM32 IC to vastly reduce size:
  Merge internals, LiDAR sensor, and motor assembly
  Could be run off a rechargeable Li-ion internal battery
  Machine body from aluminum via CNC to greatly increase resiliency
Arduino NANO, A4988 driver, and DC power inputs soldered to 5x7cm perfboard for permanent mounting/wiring
GUI buttons soldered to 2x8cm perfboard
Wire connections between Arduino and LCD screen/buttons can be disconnected for servicing/troubleshooting
Powered via dual-output USB battery bank for 5V and 12V circuits
While in “focus mode”, live distance feed from TF-Luna is listed on screen
TFMPlus Arduino library used for TF-Luna serial communication
AccelStepper Arduino library used for speed-ramped stepper motor control
LiquidCrystal_I2C Arduino library used for LCD display communication
Control box and LiDAR sensor block mounts to cinema camera rig using standardized ¼-20 screw mounts
Focus motor attaches to standardized 15mm mounting rods to interface with focus ring via 0.8 Mod gear
Total materials cost of only $71.69 per unit
Motor Position Instructions
Motor
Signal
Open/Closed Switch Data
Sensor Block
Control Box
Motor Block