## Slide 1: Electrosonics Building Renovation and Remediation Dennis Chase | Jayleigh Genest | Paige Hornbeck | Mason Pillsbury | Jacob Ritchie Civil and Environmental Engineering, University of New Hampshire, Durham, NH 03824
Decision Matrix
Introduction
Structural Details
Acknowledgements
Existing Conditions
Background: The Town of Chesterfield, with the Chesterfield Revitalization Group, and the New Hampshire Department of Environmental Services, requests a redevelopment of the former Electrosonics building and property on NH Route 9A to be redeveloped. The building is experiencing severe structural deterioration after being abandoned for 30 years and has a variety of contamination concerns after a history of industrial use.
Goal: Provide the town with a recommendation for the building usage with a proposed structural design to restore the existing building, along with a site remediation plan to address contamination concerns. The scope includes site visit observations, a code review of the existing structure, proposed alternative design development plans, structural renovation calculations, calculated cost estimates, and environmental remediation schematics.
The structure has extreme deterioration, including corroded metal decking, rotting wood framing, and toxic organic growth on the brick masonry. Testing found bulk moisture, asbestos, lead paint, and PCBs within the building. The site has severely limited space, posing challenges for site expansion.
Sydni Clark: Project Sponsor, Weston & Sampson
Alissa Reitter: Project Sponsor, Weston & Sampson
Lisa Damiano: Faculty Advisor
Kenneth Flesher: Faculty Advisor
Cost Estimate
References
AISC 16th Edition Steel Construction Manuel
ASCE 7-16 Minimum Design Loads for Buildings and Other Structures
2021 International Building Code
Phase II Environmental Site Assessment and Hazardous Materials Inventory (2013) by Ransom Consulting
Design
Environmental Remediation
Soil Testing
(1 per 200
= 17 tests)
Item | Estimated Cost
Environmental | $615,000
Demolition/Cosmetic | $196,000
Structural | $703,000
Site/Interior | $919,000
Total | $2,433,000
Consideration | Elderly Housing | Café / Apartment | Pub / Function Room
Usage / Parking Needs | 3 | 2 | 1
Town Interest / Benefit | 1 | 2 | 3
On-Site Wastewater Treatment System | 2 | 3 | 1
Economic Viability | 1 | 3 | 2
Total | 7 | 10 | 7
In the table above the highest score indicates the most preferred. The image was AI generated using Canva Magic Media, producing an example of the envisioned interior design.
Sample Floor Plan
Reinforcement to strengthen the existing steel beams
Sample Structural Plan
Modeled 3D Structure
Google Earth image with marked areas of concern proposed for excavation
3D model of the existing site
Backfill +
grading
(3300 )
The building has had multiple prior usages resulting in significant quantities of electroplating metals and solvents being discharged into the ground and multiple fuel oil spills. The surrounding soils and ground water are contaminated with cVOCs, RCRA metals, and petroleum. Below outlines the recommended remediation process.
Excavation: clean + contaminated soils
(3300 )
On-site soil
staging (10 dumpsters)
Transportation and landfill disposal
(1500 )
Grading,
loam + seed
(10000 )
Clean fill with
trucking
(1500 )