## Slide 1
ULTRALIGHT PROJECT
Mechanical Engineering, University of New Hampshire, Durham, NH 03824
Marcus Herold, Seth Chartier, Philip Mather, Ethan Tillinghast, Brian Viscido
Faculty Advisor: Dr. Ivaylo Nedyalkov
Analysis
Our Mission
Driven by a commitment to innovation and sustainability, our undergraduate team combined hands-on engineering, modeling and experimentation, becoming the first in the world to successfully design, build, and fly a manned electric ultralight aircraft. As one of the last major modes of transportation to electrify, aviation is on the verge of transformation — and we aim to be at the forefront of that change.
Major Constraints
Adhere to all legal requirements.
  254 lbs weight limit
  24 knots maximum stall speed
  55 knots max speed
Aircraft must take off under its own power.
Aircraft must not experience any structural damage at any point during flight.
All critical components rated to 2.5g load with 1.5 FOS.
Experimentation
Wing Structural Testing
  Wings loaded to 2.0 G’s to simulate worst-case in-flight conditions.
    Observed no failure of Kevlar cords and no yielding or plastic deformation in aluminum spars.
Dynamic Thrust Testing
  Data collected from a calibrated load cell to evaluate performance of various motor-prop configurations.
    A range of speeds and power settings were used to characterize thrust output under dynamic operating conditions.
Flight Plans
Sky Haven Airport Rochester, NH
Wright-Brother’s style flight
Winds < 10 kts, <5 kts crosswind component, no precipitation, daylight
Pilot
Certified Pilot Zack Yeaton.
205 Flight Hours
Instrument Rated
Experience flying many aircraft styles including traditional and taildragger configurations.
Acknowledgements
Advisor: Ivaylo Nedyalkov
TSC workers: Scott Campbell, Noah McAdam, Kevan Carpenter
CEPS Dean: Erin Bell
Department Chair: Christopher White
Professionals: Todd Scruton, Jeff Sullivan
Academic Provost: Cyndee Gruden
UNH Legal: Karyl Martin, Debbie Grotheer
Wings
Epler 1210 profile cut from foam and fiber glassed. Two aluminum spars for strength.
Landing Gear
Bungee design allows for smooth landing and adjustable tension.
King Post
Custom pulley design 8x multiplies forces to tension wings.
Kevlar Rigging
Wings rigged with 400lb Kevlar to transfer load from wing to frame.
Empennage
Constructed from pine wood. Adhered together with glue, laser cut gussets and wood screws.
Power System
20-kW Motor
111 Nominal Voltage Battery
VESC Speed Controller
CFD Analysis
Varying angles of attack analyzed
In and out of ground effect flow
Covered and uncover fuselage
  Conclusions
110 lbf of drag
450 lbf of lift
Conclusions:
All experimental joints required a higher breaking force than SolidWorks predicted.
Inset and outset gussets proved to require comparable breaking forces
Impact Load Analysis
Main landing gear designed to withstand 2.0 G landing
Energy balance used to calculate impact speed according to the FAA.
Fuselage
¾” cold-rolled steel welded in house.
Material Challenges
Experimental
Computational
Weight Budget
Met weight constraint with 2lbs to spare.
Item | Weight (lbs)
Fuselage | 65
Wings | 70
Power System | 61
Empennage | 34
Miscellaneous | 22
Total | 252
Gusset Type | Breaking Force | 
 | Analytical (lbs) | Experimental (lbs)
45° Inset | 65.0 | 127.3
45° Outset | 57.2 | 167.7
90° Inset | 43.5 | 220.5
90° Outset | 47.5 | 136.6