## Slide 1
Fatemeh Hosseini1(Fatemeh.HosseiniBaharanchi@unh.edu), Wei Sun1, Ahmad Mehrabi2 , Jo E. Sias1, Mohamed Elshaer1, Eshan V. Dave1
1University of New Hampshire, USA; 2California Department of Transportation, USA
A Methodology to Account for Rising Groundwater in Flexible Pavement Analysis and Design
The Eq-MR framework links groundwater elevation → saturation → MR → pavement response using SWCC to Witczak moisture and MR models, and LEA.
Simple polynomial Eq-MR-GWT relationships are provided for all AASHTO soil classes, allowing designers to plug rising GWT into AASHTO 1993 and M-E tools without changing the core software.
Application examples show that rising GWT can significantly reduce PSI-based life and rutting life, while having a smaller impact on fatigue life for the investigated section.
The method offers a practical way to incorporate climate-driven groundwater rise into current pavement design practice and resilience planning.
Future works:
  Compare Eq-MR predictions with field MR and performance under different GWT levels
  Improve moisture/damage transfer functions and include maintenance in life-cycle analysis
  Add Eq-MR and performance curves to agency decision tools for coastal/low-lying roads
Approach to Determine Eq-MR
Objectives
Motivation
Eq-MR Prediction Models
Summary of fitting parameters of the developed regression models
Example Application
Conclusions and Future works
Develop an equivalent resilient modulus (Eq-MR) methodology that converts groundwater-driven moisture changes into a single subgrade modulus value.
Provide soil-specific predictive Eq-MR models for all 12 AASHTO subgrade soil classes.
Demonstrate how Eq-MR can be used within AASHTO 1993 and M-E fatigue/rutting models to quantify the impact of rising groundwater on pavement performance.
Sea level rise and more frequent flooding are raising groundwater tables, softening pavement subgrades and shortening pavement life.
Current AASHTO 1993 and most M-E design methods only use a constant or seasonally averaged subgrade modulus and do not explicitly account for rising groundwater.
Agencies need a practical way to include groundwater-driven moisture weakening in standard design tools to improve resilience of coastal and low-lying pavements.
Convert each subgrade layer to different sublayers
Estimate SWCC from each soil type features and GWT level.
Compute degree of saturation vs depth for different groundwater table elevations.
Use Witczak-type relationships to convert saturation to MR for each subgrade sublayer.
Fit second-order polynomials relating GWT depth to Eq-MR for all AASHTO soil classes.
Use Eq-MR time series as inputs to:
  AASHTO 1993 PSI equation, and M-E fatigue and rutting transfer functions.
Run WinJULEA LEA with depth-varying MR to obtain pavement responses.
Replace layered subgrade with a single semi-infinite layer and back-calculate Eq-MR that reproduces deflection at subgrade surface.
Repeat for multiple GWT depths and soil types.
Moisture & MR Modeling
Layered Elastic Analysis & Eq-MR
Predictive Models & Design Integration
With constant GWT, PSI stays above terminal for 25 years; with rising GWT, service life reduces by ~30%.
Rutting is highly moisture-sensitive: rutting life drops to zero just after ~7.5 years under rising GWT, compared with >20 years for constant GWT.
Fatigue is less sensitive: fatigue life under rising GWT is only slightly shorter (~0.5 year) than under constant GWT for this example.
Deflection-based Eq-MR selection: highest sensitivity to rising GWT; consistent with deflection-based design practice
Eq-MR decreases as GWT rises into the transition zone; beyond a certain depth, MR is capped at the optimum design value.
second-order polynomial fits; reproduces LEA-based Eq-MR for coarse- and fine-grained soils
Equivalent MR *= (a × GWT2 + b × GWT + c) × MR,opt |  | 
Soil type | Depth of transition zone (in) | Saturated MR (psi)
A-1-a | 15.0 | 25,582
A-1-b | 15.4 | 23,993
A-2-4 | 23.6 | 20,815
A-2-5 | 16.0 | 18,114
A-2-6 | 16.2 | 16,684
A-2-7 | 16.2 | 15,730
A-3 | 24.5 | 19,385
A-4 | 141.7 | 15,544
A-5 | 126.8 | 13,026
A-6 | 225.9 | 12,155
A-7-5 | 373.8 | 8,477
A-7-6 | 614.6 | 6,261
Chart: Pavement Life (year)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Constent GWT at 25 inch from top of subgrade | 4.124 | 4.048 | 3.971 | 3.893 | 3.815 | 3.736 | 3.657 | 3.577 | 3.496 | 3.415 | 3.333 | 3.25 | 3.166 | 3.082 | 2.997 | 2.911 | 2.825 | 2.738 | 2.65 | 2.561 | 2.472 | 2.382 | 2.291 | 2.199 | 2.107 | 2.014
Terminal PSI | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Changing GWT 1 inch per year | 4.124 | 4.044 | 3.959 | 3.869 | 3.774 | 3.673 | 3.567 | 3.454 | 3.335 | 3.21 | 3.078 | 2.938 | 2.791 | 2.636 | 2.474 | 2.304 | 2.125 | 1.938 | 1.743 | 1.539 | 1.327 | 1.106 | 0.877 | 0.639 | 0.393 | 0.14
Chart: Time (year)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Constant GWT at 25 inch from top of subgrade | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25
GWT rising at 1 in per year | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
AASHTO 1993
Chart: Time (year)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
fatigue life with constant GWT | 1 | 0.87874 | 0.75747 | 0.63619 | 0.51489 | 0.39359 | 0.27227 | 0.15094 | 0.029593
fatigue life with 1 in/yr rising GWT | 1 | 0.87762 | 0.7541 | 0.62943 | 0.5036 | 0.3766 | 0.24844 | 0.1191 | 0
rutting life with constant GWT | 1 | 0.97146 | 0.94291 | 0.91437 | 0.88582 | 0.85726 | 0.82871 | 0.80015 | 0.77159 | 0.74302 | 0.71445 | 0.68588 | 0.65731 | 0.62873 | 0.60015 | 0.57157 | 0.54299 | 0.5144 | 0.48581 | 0.45722 | 0.42862 | 0.40002 | 0.37142 | 0.34282 | 0.31421 | 0.2856
rutting life with 1 in/yr rising GWT | 1 | 0.95982 | 0.9046 | 0.83031 | 0.73218 | 0.60464 | 0.44128 | 0.23472 | 0
M-E Fatigue and Rutting
This work was supported by NOAA’s Coastal Communities’ Pavement Resilience to Sea Level Rise Using Natural and Nature-Based Features (Grant No. NA21NOS4780145). The views expressed are those of the authors, not the sponsoring agency.
Acknowledgment
HMA: 6-in
Base 8-in
Subgrade: semi-infinite
A-3
ESAL: 0.5 million with 1% growth
Chart: Normalized pavement responses
| 0.61618072671118695 | 0.65688309828906855 | 0.75733000623830316 | 0.80263440475338255 | 0.85874845320761273 | 0.92525285581338279 | 0.98621437264146106 | 0.99761717271918426 | 1
Deflection at top of subgrade | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
Horizontal strain at bottom of AC | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
Vertical strain at top of subgrade | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
Vertical stress at top of subgrade | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
Chart: Eq_MR (psi)
| 36892 | 33938 | 28136 | 26046 | 23798 | 21530 | 19753 | 19448 | 19385
deflection at top of subgrade | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
horizontal strain at bottom of AC | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
vertical strain at top of subgrade | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
vertical stress at top of subgrade | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
 | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
 | 39.3701 | 31.4961 | 19.6851 | 16.4055 | 13.1221 | 9.8425 | 6.563 | 3.2795 | 0
*The coefficients a, b, and c are soil-specific.
Chart: Eq-MR (psi)
| 40315.927790674701 | 38663.585485359057 | 35682.642913687501 | 32497.565545376357 | 29104.162021370204 | 25510.57
A-1-a, Prediction model | 15.0443 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-1-a, Deflection-Based calculation | 15.0443 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-2-5, Prediction model | 16.0078 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-2-5, Deflection-Based calculation | 16.0078 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-3 Prediction model | 24.496 | 19.685 | 16.4055 | 13.122 | 9.4488 | 6.563 | 3.2795 | 0
A-3, Deflection-Based calculation | 24.496 | 19.685 | 16.4055 | 13.122 | 9.4488 | 6.563 | 3.2795 | 0
Chart: Eq-MR (psi)
| 25420.955669568728 | 24998.154266999998 | 22992.776388000002 | 21204.398075000001 | 19633.019327999998 | 18278.640147000002 | 17682.825393750001 | 17141.260532 | 16747.06856448 | 16220.880482999999 | 16088.632702921444 | 15962.259956454844 | 15842.065295750001 | 15727.893579519243 | 15619.618596857044 | 15517.5
A-4, Prediction model | 141.6926 | 137.795 | 118.11 | 98.425 | 78.74 | 59.055 | 49.2125 | 39.37 | 31.496 | 19.685 | 16.4055 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-4, Deflection-Based calculation | 141.6926 | 137.795 | 118.11 | 98.425 | 78.74 | 59.055 | 49.2125 | 39.37 | 31.496 | 19.685 | 16.4055 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-6, Prediction model | 225.9287 | 196.85 | 177.165 | 157.48 | 137.795 | 118.11 | 98.425 | 78.74 | 59.055 | 39.37 | 31.496 | 19.685 | 16.4055 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-6, Deflection-Based calculation | 225.9287 | 196.85 | 177.165 | 157.48 | 137.795 | 118.11 | 98.425 | 78.74 | 59.055 | 39.37 | 31.496 | 19.685 | 16.4055 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-7-6, Prediction model | 614.6444 | 590.55 | 531.495 | 472.44 | 433.07 | 393.7 | 354.33 | 314.96 | 275.59 | 236.22 | 196.85 | 177.165 | 157.48 | 137.795 | 118.11 | 98.425 | 78.74 | 59.055 | 49.2125 | 39.37 | 31.496 | 19.685 | 16.4055 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
A-7-6, Deflection-Based calculation | 614.6444 | 590.55 | 531.495 | 472.44 | 433.07 | 393.7 | 354.33 | 314.96 | 275.59 | 236.22 | 196.85 | 177.165 | 157.48 | 137.795 | 118.11 | 98.425 | 78.74 | 59.055 | 49.2125 | 39.37 | 31.496 | 19.685 | 16.4055 | 13.122 | 9.8425 | 6.563 | 3.2795 | 0
7.5 years