## Slide 1: Trash Monsters Evan Hemingway, Ryan MacKay, Peyton Marshall Department of Mechanical Engineering, University of New Hampshire, Durham, NH 03824
Testing & Analysis
Backpack Trash Management System
References
Vehicle Trash Storage
Market Evaluation
Problem Statement: Consumers lack a clean, convenient way to store small amounts of trash while on the go, especially outdoors and in vehicles. Without dedicated solutions, waste accumulates quickly and often leads to makeshift storage or littering.
Solution: This project presents two compact solutions: a backpack-mounted waste system for outdoor use and a vehicle-based trash storage unit, both designed to enable secure and responsible waste management.
Clip Testing & Model Correlation
PLA clips modeled as cantilever beams
Static load–deflection tests for nominal (0.10 in) and ± thickness variants
Beam theory hand calcs and SolidWorks FEA used for comparison
Agreement between experimental, FEA, and analytical results
Elastic-dominant response within design load range
Nominal geometry provides balance of flexibility and durability
Surveys and observations identified primary users: hikers, backpackers, dog walkers, and travelers in low-access waste environments.
Key design requirements included hands-free use, compact form, durability, hygiene,
and Secure attachment.
Stress Whitening
Acknowledgements
Huge thanks to our faculty advisor Ivaylo Nedyalkov and our entrepreneurship mentor Corkey Newcomb. Additionally, thanks to the UNH Mechanical Engineering department and staff, along with the UNH CEPS Makerspace.
Computational Tab Analysis
SolidWorks linear static FEA
100% infill FDM models (PLA, TPU)
Fatigue estimated using Basquin S–N relationship
Conservative fatigue strength = 20% UTS at 10⁶ cycles
Load cases: 0.25–2.5 lbf
Results
0.25 lbf → FOS 6.75, infinite life
1.5 lbf → ~1.1×10³ cycles
2.5 lbf → ~1.0×10² cycles
Safe for repeated use within expected loading range
User concerns focused on comfort, odor control, and compatibility with existing gear systems .​
Analysis of existing products revealed minimal direct competition, indicating a strong market opportunity​.
Failure criteria defined by brittle fracture risk and loss of function when permanent clip deflection exceeds 0.05 in.
Experimental load–deflection response and plastic recovery behavior for PLA cantilever clips of varying thickness, demonstrating strong agreement with beam theory and FEA predictions.
Future Plans
Convert provisional patent into a full patent application and collaborate with a patent attorney .
Evaluate sustainable material alternatives to 3D printing (e.g., bamboo).
Investigate scalable manufacturing methods (e.g., injection molding)
Assess manufacturability, cost feasibility, and market readiness.​
Develop branding concepts and product identity.​
Explore business formation, including LLC registration.
Bambu Lab. PLA Basic Technical Data Sheet; TPU 95A HF Technical Data Sheet
Afrose, S., Masood, S.H., Nikzad, M., Sbarski, I., Groth, A. (2016). Fatigue behaviour of FDM PLA
Gómez-Gras, G., Jerez-Mesa, R., Travieso-Rodriguez, J.A., Lluma-Fuentes, J. (2018). FFF PLA fatigue performance
Ezeh, O., Susmel, L., Brennan, F. (2019). Raster orientation effects on PLA fatigue
Ziemian, C., Sharma, M., Ziemian, S. (2012). Anisotropic properties of FDM polymers
Marsavina, L., et al. (2021). Fatigue behavior of TPU
Alam, P., Mamalis, D., Robert, C., Floreani, C., Brádaigh, C. (2019). Fatigue of elastomers review
Boubakri, A., Haddar, M., Elleuch, K., Bienvenu, Y. (2010). Mechanical properties of TPU
Menary, G., et al. (2012). Polyurethane cyclic performance
Stephens, R.I., Fatemi, A., Stephens, R.R., Fuchs, H.O. (2000). Metal Fatigue in Engineering
Dowling, N.E. (2013). Mechanical Behavior of Materials
Receptacle Body: Compact, semi-rigid container designed to store small waste items while maintaining shape and durability during use
Living Hinge Opening: Integrated deformable opening allows one-handed, hands-free disposal without separate moving parts, improving usability and reliability
Bottom Disposal Mechanism: Sealed lower opening with removable cap enables controlled and hygienic emptying of contents
Bottom Cap Pull Tab: Allows for easy removal of bottom cap
Result: Integrated system combining accessibility, secure attachment, and user-friendly waste disposal in a compact form
Strap-Mounted Attachment: Secure clip-based system enables direct mounting to backpack straps, providing easy access and stable positioning during movement
Modular Mounting Interface: Detachable connection between container and mount allows repositioning, removal, and compatibility with different gear setups
Result: Integrated system combining accessibility, secure attachment, and user-friendly waste disposal in a compact form
Living Hinge Stress Analysis
Fatigue analysis using approximated S-N curves show that at nominal load case the living hinge is below endurance limit for TPU
Living Hinge Opening: Integrated deformable opening allows one-handed, hands-free disposal (while driving if needed).
Receptacle Body: Compact, semi-rigid container designed to store small waste items in a vehicle on the go.
Elastic Performance Analysis
Plastic Recovery Analysis
Living Hinge Stress Analysis
Conservative approx. of measured force of 1lbf applied to living hinge surface
Minimum FOS of 13
Fatigue analysis using approximated S-N curves show that at nominal load case the living hinge is below endurance limit for TPU
Mounting Clip Fatigue Analysis
Stress Analysis For Static Load