## Slide 1: Egmont Channel Range Rebuild

## Slide 2: Project Involvement
Team:
  Nicole Sanborn- Project Manager
  Ryan Boyle
  Gabe Paster
  Brian Duignan
Project Sponsor: Appledore Marine Engineering, LLC
  Thomas Ducharme
Project Advisor:
  Professor Benoit
University of New Hampshire

## Slide 3: Introduction
Background
  Range Front Light
  Range Rear Light
Design Criteria
Scope of Work
Alternatives Investigated
Final Design
Challenges
Conclusion
Questions
3

## Slide 4: Project Background
Located in St. Petersburg, Florida
Tampa Bay Port
  Florida's largest Port
  Over 5,000 acres
  Handles over 37 million tons of cargo a year
Egmont Channel
  Only entrance into Tampa Bay Port from Gulf of Mexico
Range
  Critical to aid ships into Tampa Bay Port safely
  Two well lit, fixed offshore structures

## Slide 5: Existing Range Front Light
Located 2 miles offshore
Constructed 1990
Prefabricated steel jacket structure
10 foot water depth
Focal height 30 feet above MHW (Mean High Water)
Severely corroded

## Slide 6: Existing Range Rear Light
Located 300 yards offshore
Constructed 1990
Prefabricated steel jacket structure
15 foot water depth
Focal height 115 feet above MHW (Mean High Water)
Severely corroded
Lattice Tower/Light destroyed in 2017 hurricane season

## Slide 7: Design Criteria
Criteria
  50 year design life with little to no maintenance
  100 year return period for wind and wave load
Design Concepts
  Range front light
    Monopile design
  Range Rear Light
    Multi-pile

## Slide 8: Scope of Work
Maintain regular project meetings
Continuous communication
Obtain background information
Geotechnical feasibility study for the foundation
Assess the wave loads on structure
Develop 100-year design wind and wave loads
Design range front light
Design range rear light
Perform structure life cycle analysis for 50-year
Develop construction cost estimates

## Slide 9: Potential Reef Structure
Save Money on demolition and disposal costs
Creates artificial reef for Marine organisms
Environmental Resource Permits
General Permit
Individual Permit
http://myfwc.maps.arcgis.com/apps/View/index.html?appid=4675e1db32ac43a9a4308e757965d17d

## Slide 10: Structural Alternatives
Materials:
Corrosive resistant
Handle wind and wave loads
Timber- no corrosion. Insufficient load capability
Steel- susceptible to high corrosion
High Grade Stainless- strong, corrosion resistant, $$
Steel with corrosion protection
  Epoxy coating- 5-10 years before breaking down
  Sacrificial Anodes- 5-10 years before breaking down
    More negative electrochemical potential than structure
  Sacrificial Steel on Wall thickness- to get structure to desired design life
https://www.stainlesstubular.com/bar-structural-shapes.html

## Slide 11: Corrosion Resistance
50 year design​
Probable failure of previous structure​
Wetting and drying of structure

## Slide 12: Geotechnical Alternatives
Monopile
Jacket Structure
Twisted Jacket
https://www.energy.gov/eere/articles/us-conditions-drive-innovation-offshore-wind-foundations

## Slide 13: Scour
Common problem for marine structure
Occurs when water moving past structure loosens soil around foundation below
https://www.ayresassociates.com/battling-bridge-scour-with-research-inspections-and-training/
*Example of Scour*

## Slide 14: Scour
Previous design had problematic scouring ​
Attempt was made to remediate by pouring concrete around existing piles​
Scour continued to occur

## Slide 15: Articulating Concrete Block Mattress
https://www.maccaferri.com/ae/products/articulated-concrete-block-mattresses-acbm/
https://www.conteches.com/knowledge-center/pdh-article-series/articulated-concrete-block-design
Effective and relatively easy way to fight scour
Concrete block mattress installed in all directions from structure
Mattress slopes down and reaches underneath the maximum scour expected

## Slide 16: Wind Calculation Development
Wind loads calculated using ASCE 7-10
Wind loads negligible for monopile
Cannot have wind and wave acting at same spot
Wind loads calculated by taking tower as sections
Assumed 50% cross sectional area for the tower
Taken about two directions
16

## Slide 17: Development of Wave Loading
Cyclic Loading​ (wave period)
Wave height​
Storm Surge
High water level
Sea level rise
http://www.hann-ocean.com/index.php/products/ocean.html
17

## Slide 18: Wave Calculation Development
Three types of forces from waves
  Drag
  Inertia
  Breaking wave
Breaking wave controls
Water depth affects wave loads greatly
Sea growth taken as a factor
18

## Slide 19: Soil Conditions
Four layers of sand from –15 ft MLLW (Mean Lower Low Water Level)​
Clay layer at –100 ft MLLW​

## Slide 20: Modeling Process
LPILE
Performs hundreds of iterations of the pile with soil profiles and properties input
RISA
Optimizes structure
Coupled system

## Slide 21: RISA Issues
UNH provides demo version
Saving model files
Limits extent of design
Led to adjustment of scope

## Slide 22: Coronavirus Complication
Modeling challenges
  Ten minute in person introduction prior to vacation
Adjustment to a new work environment
Lack of reliable software
No in person meeting

## Slide 23: Life Cycle Assessment
Goal in our LCA: analyze the potential environmental impacts and determine if the life cycle of the structures will meet design requirements designated by the scope
Making sure the structures are sacrificial anodes and steel with an epoxy coating
Climate change
Old Structure into a reef structure
  If not removal of old structure to reduce physical risk
Recommend same locations, same impact
Not in scope: recommend putting solar panels on the top of the structures to power the lights
http://fibrenet.eu/index.php?id=blog-post-eleven
23

## Slide 24: Conclusion
Followed scope with minor amendments
Load Development Process
Choosing the best course of action to meet our design goals
Working through challenges presented with resources available
Taking advantage of virtual connections and resources
Communication amongst group, sponsor and advisors

## Slide 25: Sources
AppledoAppledore Marine Engineering, LLC “Articulated Concrete Block Mattresses (ACBM) - Maccaferri Middle East.” Maccaferri Middle East,
www.maccaferri.com/ae/products/articulated-concrete-block-mattresses-acbm/. Coastal Engineering Manual. Coastal and Hydraulics Laboratory, U.S. Army Engineering Research and
Development Center, Waterways Experiment Station, 2004. Coulbourne, William L, and T. Eric Stafford. Wind Loads: Guide to the Wind Load Provisions of ASCE
7-16. American Society of Civil Engineers, 2020. Minimum Design Loads and Associated Criteria for Buildings and Other Structures. American Society of
Civil Engineers, 2017. “U.S. Conditions Drive Innovation in Offshore Wind Foundations.” Energy.gov,
www.energy.gov/eere/articles/us-conditions-drive-innovation-offshore-wind-foundations

## Slide 26: Acknowledgements
The project team would like to express thanks to the project sponsor and advisor, Thomas Ducharme and Jean Benoit for the continuous support and guidance they have provided thus far for this project. The team would also like to thank Raymond Cook for his help with the understanding of foundation and structure alternatives, Majid Ghayoomi for his help with structural elements, and Thomas Ballestero for his help with load development. This project and its development would not have been made possible without the resources or help provided by the University of New Hampshire.

## Slide 27: Questions?
CEE 797 - 4 Presentation Skills.pdf
CEE 797 - 4 Presentation Skills.pdf
Please feel free to send any questions to:
nss1007@wildcats.unh.edu