## Slide 1: Zero Waste Transfer Station Whitefield, New Hampshire Department of Civil and Environmental Engineering, University of New Hampshire, Durham, NH 03824
Current Facility Concerns:
  Operation Inefficiencies
  Environmental Impacts
  Community Access
  Increased MSW disposal costs
Transfer Station Design Alternative I
Site Background
Existing Policy
Proposed Policy
Market Research
Pay-As-You-Throw Incentive Program
  Reduces amount of recyclable material entering the waste stream
  Achieves higher material purity
Aerial
Recommendations
Conserve energy by utilizing an existing building
17,000 square feet of solar panel potential.
Central location in Whitefield, within proximity of downtown.
Restore a deteriorating building, add value to the neighborhood
Whitefield must educate residents to initiate Zero-Waste, public support is necessary
Bi-Lane drive in drive out is most economical and efficient retrofit determined
Conclusion
Defining Zero Waste
Disposal cost of $67 per ton of MSW (Transportation fee $6.75 per ton)
Average composition of municipal solid waste
Paper and cardboard: 25%
Glass: 4.2%
Metals: 9.4%
Plastics: 13.2%
Yard Trimmings: 13.1%
Wood: 6.7%
Rubber and Leather: 3.4%
Textiles: 6.3%
Other: 1.9%
Misc. Inorganic Wastes: 1.5%
Whitefield MSW was 30 tons in a month
If recycled and sold at average market value
Costs $363.45 a month to dispose of MSW to landfill
If all MSW goes to a landfill
Costs $2212.50 a month to dispose of MSW to landfill
Recycling saves $1849.05 per month.
Note: Figures are a best-case scenario
Population: 2,213
Median Age: 51 years
Median Income: $32,893
Implementation of a new facility achieves:
Diversion of 75% of waste by weight as recyclable material
Remaining 25% of waste disposed of in a landfill
Draft
Draft
Drive in- drive out facility
Bi- lane traffic
Left lane to dispose of larger wastes
Right lane to dispose of recyclables
Design I alleviates Whitefield’s concerns
A bi-lane traffic pattern smoothens operations and allows for a higher volume of flow
The tipping floor is spacious for adequate work areas
Stricter separation at the household level
Use of educational material
Higher Value Incentives
Clear and concise ordinance documents
Chart: Estimated MSW Disposal Costs
| Estimated MSW Disposal | Potential Recycleable Revenue | Projected Disposal Cost after Revenue
 | 2212 | -1849 | 363