## Slide 1: Riverwalk Pavilion
Team 22 – Jamie Fitzpatrick (PM), Griffin Curley, Jared Grondin, Oliver Roy, Jack Sargent, and Michelle Thibault
Project Sponsor – The Engineering Corp
Sponsor Contact – Chris Raymond
Project Advisor – Anthony Puntin
Notes: Jamie

## Slide 2: Introduction and Background
Existing Lot
4.67 acres
Lawrence, MA
Riverwalk Engineers proposed design
Notes: Jamie

## Slide 3
Locus Map of Project Site
EXIT 44
N
Notes: Michelle

## Slide 4: Scope
Develop a site concept
Perform structural and geotechnical calculations
Provide architectural renderings
Develop a transportation plan
Address floodplain issue
Notes: Michelle

## Slide 5: Program
4-Story Multi-Use Building with 60,000 SF Total Floor Area comprised of:
  7,500 SF Retail Space
  7,500 SF Restaurant Space
  30,000 SF Office Space
  15,000 SF Function Space
Parking Garage
Multipurpose Athletic Field
Notes: Oliver

## Slide 6: Site Visit
Transformer – cannot be moved
Notes: Oliver

## Slide 7: Parking Requirements
Required Parking from Lawrence, MA zoning regulations:
Function Hall: 75 spaces
Retail: 30 spaces
Restaurant: 25 spaces
Office: 90 spaces
Existing Lot: 500 spaces
Field: 120 spaces
Total: 840 spaces
Notes: Jack

## Slide 8
Parking Layout
Location of Transformer
Exit
Entrance/Exit
Notes: Jack

## Slide 9
Plan View of Proposed Structure
N
Road
Riverfront pathway
Multi-purpose building
Lot Entrance and Exit
Athletic Field
Notes: Jack

## Slide 10: 3D Modeling
Features:
Fourth floor curtain walls
Optimum roof for solar panels
Rooftop Deck
Walking path along river
Notes: Jack

## Slide 11: 360° View of model (Video)
Notes: Jack

## Slide 12
Rendering + Satellite
Notes: Jack

## Slide 13
Column Layout
Exit
Entrance/Exit
Notes: Michelle

## Slide 14
Structural Design Process
Assumed a typical floor system
  Inverted T-beam spanning 36 feet E/W
  Joist spanning 60 feet N/S
Calculated column loads based on ASCE 7-10
Final design:
30in by 30in RC column (10 ksi)
#10 Main Bars and #4 Tie Bars (75 ksi)
Notes: Jamie

## Slide 15
Geotechnical Design Process
Used column loads based on ASCE 7-10 and self weight of the column designed
Reviewed geotechnical report to evaluate soil conditions
Used toe bearing and side friction equations to design a driven pile in the drained condition
Calculated a required cross sectional area for a concrete driven pile
Final Design:
30 inch diameter concrete pile
1 pile per interior column
Notes: Michelle

## Slide 16
Locus Map of Project Site
EXIT 44
N
Notes: Michelle

## Slide 17
Transportation Design Plan
Traffic Flow into Site
Traffic Flow out of Site
1
2
3
1
2
KEY:
N
Notes: Jared

## Slide 18: FEMA Flood Map

## Slide 19: Floodplain Considerations
Found the 100-year flood elevation and the elevation of the site​
Calculated volume displaced
Options for compensatory storage:
      Depressing the parking garage
      Excavating a large hole to compensate
      A continuous catch basin around the perimeter of the building
Notes: Jack

## Slide 20: Challenges Encountered
Site Design
  Existing utilities relocation
  Setbacks and space constraints
  Pedestrian/vehicle transportation around the structure
Floodplain location
  1,222 cubic yard of water is displaced for a 100-year flood
Structural
  Calculating the moment at the top and bottom of the column
Geotechnical
  Determining soil properties
Notes: Oliver

## Slide 21: Thank you!
Please contact us with any questions involving the Riverwalk Pavilion at:
jmf1037@wildcats.unh.edu , Jamie Fitzpatrick (Project Manager)
met1019@wildcats.unh.edu , Michelle Thibault
jrg1038@wildcats.unh.edu , Jared Grondin
gc1036@wildcats.unh.edu , Griffin Curley
jjs1036@wildcats.unh.edu , Jack Sargent
or1008@wildcats.unh.edu , Oliver Roy
Notes: Jamie