## Slide 1: Rennie Road 1,4 - Dioxane Groundwater Remediation
Project Manager: James Murphy
Project Members: Patrick Hamill, Zac Harvell, Lucas Theoharidis, Josh Thibeault
1

## Slide 2: Outline
Introduction
Summary of Completed Work
Site Plan/ Soil Hydraulics
Permitting
Well Design
Treatment
Conclusion
2

## Slide 3: Introduction
Site Location: Rennie Road Hanover, NH
Contaminant: 1,4 Dioxane
Challenges:
  Location
  Gradient
  Proximity to water bodies
3
Figure 1: General Contamination Area
Figure 2: Source Location and Groundwater Flow Direction

## Slide 4: Summary of Work
Phase 1
  Request for information (RFI)
  Feasibility study
    Pump and Treat
  General site plan
Phase 2
  Conceptual site plan
  Soil hydraulics
  Extraction Well Design
  Permitting
  Treatment
4

## Slide 5: Site Plan
-Elevation Map -Bedrock Map
Flow Direction
Flow
Direction
9 Rennie
Road
9 Rennie
Road
Elevation map used to understand steep slopes
Bedrock elevation map used to understand extent of plume
5
Figure 3: Contour Map
Figure 4: Bedrock Map

## Slide 6: Site Cross Section
Help to understand:
Well lengths
Visualize Flow
9 Rennie Road
6
Figure 5: Cross Section Location
Figure 6: Cross Section

## Slide 7: Groundwater Elevations
Groundwater elevations plotted on GIS
Used to make water contour map to find hydraulic gradient
​9 Rennie Road
​9 Rennie Road
7
Figure 7: June Groundwater Elevations
Figure 8: October Groundwater Elevations

## Slide 8: Soil Hydraulics - Hydraulic Gradient
Slope between monitoring wells
Monitoring well data provided by GZA
Contours drawn based on water table elevation data
Slope calculated between contours and monitoring wells
Geometric mean: 0.0468
8
Figure 9: Groundwater Elevations Contour Map

## Slide 9: Soil Hydraulics - Hydraulic Conductivity
Velocity of groundwater
Assumed site conditions were unconfined
  Unreasonable values
  Optimized K value based on 50 ft ROI
9
Figure 10: Well Model

## Slide 10: Plume Dimensions
Width of plume: 450 ft
  Estimated based on GIS map
Depth of contamination: 69.2 ft
  Calculated from soil boring logs
  Average depth to bedrock
Cross sectional area: 31140 ft2
10
Figure 11: Contamination Plume Map

## Slide 11: Required Permits
PERMIT | REASONING
Alteration of terrain | Road construction
Pump installation | Installation of pumps for treatment system
NPDES surface water discharge | Needed to protect the stream and marsh within the GMZ
Groundwater discharge | Needed for discharging treated effluent back into groundwater
Treatment | Required for treatment system operation
Stormwater site design | Site erosion will change as a result of road construction
Wetlands | The GMZ is in a wetland area
Env-wt 100-900
env-wq402
Env-OR600
11
Table 1: Required Permits

## Slide 12: Permitting-ENV OR600
Must define a groundwater management zone (GMZ)
Requirements
Tax parcel 013-014
Water bodies and properties within 500ft
Roads within 1000ft
12
Figure 12: GMZ Map

## Slide 13: Well Placement
Due to motivation only three wells will be installed
Prevents further spread of 1,4 - dioxane
Intercept main plume
Avoid spread to stream
13
Figure 13: Well Location Map

## Slide 14: Well Design
Based on soil gradation of sand, loam, and a combination of the two to simulate glacial till
Total Diameter including well pack: 6”
Will use 6" auger
Pump Rate (gpm) | 0.1
Upper Casing/Pump Housing | 
Nominal Diameter of Pump Bowl (inches) | 4
Casing Diameter (inches) | 5
Screening | 
75% of plume thickness screened | 
Slot Width (inches) | 0.008
Well Filter Outer Diameter (inches) | 2
Well Filter Inner Diameter (inches) | 1.75
14
Table 2: Well Design

## Slide 15: Treatment Options
Treatment Method | Pros | Cons
Hydrogen peroxide with UV Radiation | Proven to treat 1-4 Dioxane as well as other contaminants Moderate Capital Cost | Expensive O&M cost Must be pretreated to deal with turbidity Hydrogen peroxide residuals can pose safety risk
Hydrogen peroxide with Ozone | Proven to treat 1-4 Dioxane as well as other contaminants Moderate Capital Cost | Expensive O&M cost Hydrogen peroxide residuals can pose safety risk Bromide will oxidize to bromate requiring further treatment
Resin Treatment | Very Low O&M cost Modular/easily sized based off influent flow Small changes to influent flow will not affect levels of treatment Simple operation/will not require expensive employees | Expensive capital cost
15
Table 3: Compared Treatment Processes Pros and Cons

## Slide 16: Treatment Decision
Resin treatment - Ambersorb 560
High capital cost, but very small O&M cost will result in saving money over the years
No electricity needed for treatment
No pre/post treatment necessary
16
Figure 14: Ambersorb 560 Resin

## Slide 17: Treatment Flow Chart
Pump
Screening
To Treatment Facility
Flow through Ambersorb 560 (resin)
Pump back on-site using injection wells
17
Figure 15: Treatment System Flow Diagram

## Slide 18: Final Design
Pump and Treat
  3 Wells
Resin treatment
18
Figure 16: Well CAD Drawing

## Slide 19: Acknowledgements
Faculty advisor - Dr. Paula Mouser, P.E.
GZA GeoEnvironmental Inc.
Steven Lamb, P.G.
James Wieck, P.G.
19

## Slide 20: Questions?
20
jrm1047@wildcats.unh.edu