## Slide 1: CYCLOTRON ELECTRODE COOLING TEST Christen Gallant
View of dee plate from inside vacuum chamber with power feedthroughs.
Advised by Ivaylo Nedyalkov & Andre Chouinard
Mechanical Engineering
University of New Hampshire, Durham NH & Antaya Science and Technology, Hampton, NH
1. Dee Plate
2. Kapton Heater
3. Foot
4. Stem
5. Nichrome Wire Heater
6. Plug
7. Cooling Lines
8. Retaining Clips
9. Temperature Sensors
Legend
Design Requirements
Material & mass properties held relatively constant with cyclotron build design.
Test fixture component geometry replicated for thermal distribution accuracy.
Power distribution consistent with projected model
Testing under vacuum pressure ≤ 5 * 10-4 bar.
Test Assembly
Nichrome wire heater mounted to test fixture using varnish & cigarette paper (above left) and then wrapped with braided fiberglass insulation (above right).
In and out-flow cooling lines exiting the test fixture through the plug, mounted in CF flange.
(Left) Turbo pump backed by mechanical pump to maintain vacuum pressure.
Variac on left used to control power to Kapton heater on dee plate, Variac on right used to control power to nichrome wire heater on stem.
Model of test fixture mounted in vacuum chamber.
Background
Cyclotron – particle accelerator that produces a charged particle beam. Operates under vacuum at cryogenic temperatures (125 K 0 K)
Cyclotron use ranges from industrial to nuclear medicinal. Antaya specializes in the design of compact cyclotrons for on-demand radiopharmaceutical production (PET Scans).
In Antaya’s newest build, the electrode & stem assembly see combined power input of 350 W.
Proper cooling of multiple electrodes is necessary for functionality and efficiency.
Results
Power Correction Curve
Temperature & Power vs Time
Power Input & Heat Removal Comparison
Conclusions
Temperature at each sensor location was recorded and plotted with corresponding power input.
Combined power input plotted with calculated heat removal to confirm cooling.
With uncertainty from measurement devices accounted for, it was confirmed that the cooling method successfully removes all heat added into the system.
Test Setup
Objective
Design a test to confirm the proposed cooling method will effectively cool the electrode & stem.
Analyze the steady state temperature distribution under maximum power conditions.
2
9
1
8
9
4
5
6
7
3