## Slide 1: Water Electrolysis
Alice Wade and Ian Bresnahan
Project Outline
Create a miniature water electrolysis reactor
Converts Water into 2H2 and O2
Synthesis of rocket fuel using resources that could be found on Mars

## Slide 2: Project Purpose
In-Situ Resource Utilization (ISRU)
Sabatier Reactor
Future generation of rockets

## Slide 3: The Chemistry
Overall
2H2O → O2 + 2H2
Cathode
4H2O + 4e- → 2H2 + 4OH-
Anode
4OH- → O2 + 2H2O + 4e-

## Slide 4: Solidworks Model
Seperate tanks for hydrogen and oxygen
Clear lexan used for building main reservoir
Graphite used as electrodes
Wooden frame for structural stability & ease of transportation

## Slide 5: Test Tank Setup
Plastic bin with electrodes siliconed in
DC power supply used to provide current
Measured volume of gas produced using graduated test tubes
Table salt used as electrode to increase water conductivity

## Slide 6: Research Conducted and Data Collection
Data Collection
Ratio of Electrolyte vs. Amperage
Electrolyte → Conductivity → Speed
Explanation
Volume of Hydrogen Displaced vs. Time
Gas production results

## Slide 7: Final Reactor Components
Reservoir waterjetted out of clear lexan sheets and siliconed in place
Wooden frame cut with table saw and jigsaw
Tank made with clear acrylic tubing, 3D printed adapters, and a hose clamp
Pipe fittings used to connect tank with reservoir through a quick-disconnect system

## Slide 8: Conclusion
What We’ve Learned
Designing components which must be watertight and corrosion resistant
Engineering an assembly to facilitate and collect the results of a chemical reaction
Taking an idea from paper to a final product