## Slide 1: Controlled laboratory experiments on the dissolution of hydrate-free and hydrate-coated gas bubbles in water
Alexandra M Padilla1,2, William F Waite3 and Thomas C Weber1,2
1 School of Marine Science and Ocean Engineering, University of New Hampshire, Durham, New Hampshire, USA 2 Center for Coastal and Ocean Mapping, University of New Hampshire, Durham, New Hampshire, USA 3 United States Geological Survey, Woods Hole, Massachusetts, USA
Background
Xenon Hydrate, not Methane
Objective: Track the evolution of free-gas and hydrate covered bubbles
Methodology
Results
Imaging System
P-T Experimentation Region
Xenon was used as a proxy for methane during this experiment because though both gases form structure I hydrate, xenon hydrate can be formed at relatively lower pressures (Fu et al., 2019), allowing the counter-flow device to be made of clear acrylic for multi-directional viewing of the bubble.
Two high-speed, high-resolution imaging cameras, arranged at 90 degrees to each other, were used to obtain measurements of bubble size, rise velocity, mass transfer coefficients and bubble shape. The images were calibrated with images of a grid that had a 1/10-inch separation between grid points.
Methane is released into the ocean from the seafloor in the form of gas bubbles, which transports methane through the water column and potentially into the atmosphere. A rising
Bubble Dissolution
Rise Velocity
No Hydrate? But I am in the P-T Region…
Question: How does hydrate affect the fate and transport of methane bubbles in the water column?
Flow Loop Device
Gas bubbles were created using an ISCO pump to create a differential pressure between the water and the gas. A solenoid valve was used to briefly release a controlled amount of gas into the flow loop to create single bubbles.
Westbrook et al., 2009
Padilla et al., 2019
methane bubble loses methane to the surrounding water via methane dissolution through the bubble surface. However, when methane gas bubbles are released at certain elevated pressures and reduced temperatures, they can form a solid gas hydrate that coats the bubble surface. This hydrate coating slows down the dissolution process and can extend the lifetime of the bubble within the water column. Researchers have developed mathematical models to track the fate of methane transported from rising bubbles in order to understand the fate of methane released into the
water column as a function of depth. Tracking methane in this way is important in determining how dissolved methane concentration in the water column contributes to ocean acidification and reduced dissolved oxygen levels.
Gas bubble dissolution models have been developed, by different researchers, to study the evolution and transport of methane (or other gases) as these bubbles rise in the water column. The mass transfer of gases by dissolution can be expressed mathematically using the Ranz-Marshall equation (Ranz and Marshall, 1952):
Bubble Size
Shrinkage Rate
Mass Transfer Coefficient
Hydrate Detachment
In order to model the mass transfer of gases within a bubble, we need to have a good understanding of the size of the bubble, the background dissolved concentration and the saturation concentration of the gas in the medium, and the mass transfer coefficient.
Olsen et al., 2017
Acknowledgements: This research was funded with the USGS-DOE Interagency Agreement DE-FE00-23495 and by the National Science Foundation Graduate Research Fellowship Program and Graduate Research Internship Program. The authors would like to thank Paul Lavoie and Emile Bergeron for their help designing and constructing the flow loop device.
Goal: Determine the mass transfer coefficient of free-gas bubbles and hydrate covered bubbles.
This study will obtain estimates of the mass transfer coefficient of the free-gas and hydrate coated bubbles by collecting images of single bubbles as they dissolve..
Bubble Evolution
Air
Hydrate
Hydrate Dissociation
at Lower Pressure
Xenon
Methane
The Many Shapes of Hydrate Bubbles
New Hampshire Land Acknowledgement: The work presented takes place on N’dakinna, which is the traditional ancestral homeland of the Abenaki, Pennacook and Wabanaki Peoples past and present. We acknowledge and honor with gratitude the land and waterways and the alnobak (people) who have stewarded N’dakinna throughout the generations.
-- Clean bubble models
- Dirty bubble models
-- Clean bubble models
- Dirty bubble models