## Slide 1
Over a bridge’s service life, physical damage, such as material deterioration, accidental impact, and overloading, can decrease its load-carrying capacity. To assess the integrity and serviceability of in-service bridges, accurate and efficient structural health monitoring is required for as frequent intervals as feasible. Based on an integrated decision-making protocol, collected dynamic-response data of a bridge can be postprocessed continuously to notify the bridge owners of any noticeable change in the in-service condition of the structure. Therefore, the location and severity of damage can be determined, and the bridge load-carrying capacity based on the given damaged component(s) is calculated. The case study for this protocol is an instrumented vertical-lift truss bridge, the Memorial Bridge in Portsmouth, NH subjected to some simulated damage scenarios. For both the healthy and simulated damage conditions, a verified structural model is used as a baseline to investigate the bridge load-carrying capacity according to current standards for load resistance factor-rating approach. Once the source of the damage is identified, the impact on the bridge performance must be assessed. The accepted means for this assessment is to calculate the load rating according to the AASHTO Manual for Bridge Evaluation. The Load and Resistance Factor Rating (LRFR) method defines three distinct levels of evaluation: design-load rating, legal-load rating, and permit-load rating. The focus of this study is on the design inventory level rating factor using an HL-93 live load and the strength design 1 load combination. To predict whether the damaged members of the bridge satisfy the AASHTO design specifications for the effects of axial forces and bending moments, analytical investigations are performed for different percentages of damage.
Memorial Bridge
Results
Decreased Load-Carrying Capacity Assessment of a Vertical-Lift Steel Truss Bridge
By: Milad Mehrkash
Advisor: Prof. Erin Santini-Bell
Department of Civil and Environmental Engineering, University of New Hampshire
Bibliography
Introduction
Load Rating
- Vertical-lift steel truss bridge
- Over the Piscataqua River
- Between Portsmouth, NH & Kittery, ME
Graph Notes
Acknowledgment
Photo: Courtesy of HNTB
Analytical Model of the South
Span and Tower of the Bridge
Structural Modeling
Simulation of Damage Scenarios
(A) Truck Accident
(B) Vessel Collision
(A)
(B)
Photo: Courtesy of HNTB
Capacity of the Member
Dead Load Effect
Wearing surface & Utility Dead Load
Live Load Effect
Dynamic Load Allowance
Load Factors
Condition Factor
System Factor
Resistance Factor
Conclusions
(a) diagonal axial-based capacity reduction factor due to truck accident
(b) diagonal axial-based capacity reduction factor due to vessel collision
(c) bottom chord axial-based capacity reduction factor due to vessel collision
(d) diagonal bending-based capacity reduction factor due to truck accident
(e) diagonal bending-based capacity reduction factor due to vessel collision
(f) bottom chord bending-based capacity
reduction factor due to vessel collision
- AASHTO. 2014. LRFD Bridge Design Specifications. 7th ed. Washington DC.
- Damage detection and decreased load-carrying capacity assessment of a vertical-lift steel truss bridge, Shahsavari, V., Mehrkash, M. and Santini-Bell, E., J. Perform. Constr. Facil., 2020, 34(2): 04019123
- The greater the damage level, the
smaller the load rating due to the damage.
- The load rating is more affected
by reduction factors based on the axial strength of diagonals
compared with their flexural capacities.
- The load rating drops below 1 only for very high percentages of damage, which demonstrates that the bridge is overdesigned.
- The bridge load rating shows more sensitivity to the damage of bottom chord than the damage of the diagonal member.