## Slide 1
Controlling Hydrogen Sulfide Releases in Augusta, ME Sewers
Jessica Buhrle1, Gage Moran1, Shane Fillion1, M. Robin Collins, P.E.2
1Environmental Engineering, Dept. of Civil and Environmental Engineering, University of New Hampshire
2Professor, Dept. of Civil and Environmental Engineering, University of New Hampshire
Acknowledgments
Brian Tarbuck and Andy Begin of Greater Augusta Utility District
Professor M. Robin Collins
University of New Hampshire, Department of Civil and Environmental Engineering
The five chemical treatment compounds investigated that raise oxidation-reduction potential were: sodium nitrate, calcium nitrate, potassium nitrate, hydrogen peroxide, and oxygen (aeration). Balanced redox equations were calculated to obtain a molar ratio of treatment type to hydrogen sulfide. Dosage plots were constructed to show the concentration of chemical treatment required to remove a concentration of hydrogen sulfide in the wastewater.
    The goal of this project was to compile and compare treatments that control hydrogen sulfide while considering efficiency, cost, and convenience. Methods of doing so are:
    Raise pH to the 8.0 to 8.5 range where different sulfur species exist
    Raise oxidation-reduction potential by adding chemical oxidants or aeration
    A combination of raising pH and redox potential
Project Overview
Project Objectives: Explore Potential Solutions to Control H2S Related Issues
1. Raising pH
Compound to Reduce H2S | Redox Reaction Oxidizing H2S to S and SO42- | Molar Ratio (Compound/H2S)
Sodium Nitrate | 2H2S (aq) + 5NaNO3 + 4H2O → S + SO42- + 5NO2- + 5Na+ + 5H2O + 2H+ | 5/2
Calcium Nitrate | 2H2S (aq) + Ca(NO3)2 + 4H2O → S + SO42- + N2 + Ca2+ + 6H2O | 1/2
Potassium Nitrate | 2H2S (aq) + 5KNO3 + 4H2O → S + SO42- + 5NO2- + 5K+ + 5H2O + 2H+ | 5/2
Hydrogen Peroxide | 2H2S (aq) + 5H2O2 + 4H2O → S + SO42- + 10H2O + 2H+ | 5/2
Oxygen (Aeration) | 3H2S (aq) + 3O2 + 4H2O → 2S + SO42- + 6H2O + 2H+ | 1/1
Compound to Raise pH | Chemical Formula | Equation
Lime | Ca(OH)2 | Ca(OH)2 + 2H2S (aq) → Ca2+ + 2HS- + 2H2O
Caustic Soda | NaOH | NaOH + H2S (aq) → Na+ + HS- + H2O
Magnesium Hydroxide | Mg(OH)2 | Mg(OH)2 + 2H2S (aq) → Mg2+ + 2HS- +2H2O
Future Recommendations
3. Raising pH and ORP
2. Raising Redox Potential (ORP)
1.
2.
3.
Hydrogen sulfide is an acid, meaning it wants to donate a proton (H+). A base, which is a substance that can accept this proton using a hydroxide ion (OH-) to create H2O, can be added to Augusta’s wastewater to raise pH. The figure to the left shows H2S losing a proton to create HS- at pKa1 (pH = 6.99), and HS- losing a proton to create S2- at pKa2 (pH = 12.92).
Predominance diagram showing which species of sulfur will dominate at various pH and redox potential (Eh).
Three common compounds to raise pH in water treatment. Shows hydrogen sulfide losing a proton to create bisulfide (HS-).
Sulfide species concentration vs pH: pKa1 = 6.99, pKa2 = 12.92.
Current state of Augusta’s trunkline sewer pipes.
Process happening in Augusta’s trunkline sewer pipes.
The five ORP compounds investigated to increase oxidation-reduction potential.
Cost Comparisons
Summary Conclusions
Compound | Sodium Nitrate | Calcium Nitrate (dry, 70%) | Calcium Nitrate (wet, 20% - 40%) | Potassium Nitrate | Hydrogen Peroxide (34%)
Availability | N/A | 3,355 lb tote | 300 gal tote | N/A | 3,000 lb tote = 319 gal
Price | N/A | $0.38/lb | $6.30/gal | N/A | $0.49/lb = $4.70/gal
Price per Tote | N/A | $1,275 | $1,900 | N/A | $1,500
Totes per 30 Days | N/A | 10.2 | 17.5 – 35 | N/A | 24
Daily Price | N/A | $436.62 | $1,103 - $2,205 | N/A | $1,200
30-Day Price | N/A | $13,100 | $33,090 – $66,150 | N/A | $36,000
Compound (%) | Feed Rate – Mass Flux (lb/day) | Feed Rate – Volumetric (mL/min) | Feed Rate – Volumetric (gal/day)
Sodium Nitrate (100%) | 2,081 | N/A | N/A
Calcium Nitrate (70%) | 1,149 | N/A | N/A
Calcium Nitrate (40%) TotalOx Max, SG = 1.38 | 2,010 | 460 | 175
Calcium Nitrate (30%) TotalOx Mid, SG = 1.38 | 2,680 | 615 | 234
Calcium Nitrate (20%) TotalOx Min, SG = 1.38 | 4,020 | 920 | 350
Potassium Nitrate (100%) | 2,476 | N/A | N/A
Hydrogen Peroxide (34 %) SG = 1.13 | 2,450 | 685 | 261
Air | 1,492 | 14.62 (cfm) | 
 | Pump Setup 1 | Pump Setup 2 | Pump Setup 3 | Compressor Setup 1
Pump/Compressor | 3 x 0.11 HP | 3 x 0.33 HP | 1 x 1.0 HP | 3 x 0.33 HP
Diffuser Hose | 3 x 100 ft | 3 x 100 ft | 1 x 500 ft | 3 x 100 ft
Initial Cost | $1,741.92 | $2,151.96 | $1,454.80 | $1,965
Energy (per year) | $280.78 | $842.34 | $850.85 | $842.34
Total Cost | $2,022.70 | $2,994.30 | $2,305.65 | $2,807.34
Top considerations when researching ORP chemicals and aeration:
  Aeration is cheapest with annual costs less than $5,000 compared to over $250,000 for liquid calcium nitrate
  No storage tank or complicated feeding system associated with pump and diffuser hose aeration
  No monthly deliveries for aeration
  Dry powders are much cheaper than liquid feed, but GAUD accept the increase in price to avoid dry stock handling and feed
  pH raising compounds are frequently used in water treatment and easy to obtain
Nitrate compounds to treat a certain concentration of hydrogen sulfide.
Hydrogen peroxide and air to treat a certain concentration of hydrogen sulfide.
Feed rates to remove hydrogen sulfide, assumed flow of 4 MGD and H2S concentration of 10 mg/L.
Cost comparison of the various ORP chemical treatments.
Cost comparison of various aeration setups that meet the max demand of 14.62 cfm.
(aq)
H2
H2O
Combination (Raise pH X Raise ORP) | Equation
Magnesium Hydroxide X Calcium Nitrate | 4H2S (aq) + Mg(OH)2 + Ca(NO3)2 → S + SO42- + 2HS- + N2 + Ca2+ + Mg2+ + 4H2O
Magnesium Hydroxide X Hydrogen Peroxide | 4H2S (aq) + Mg(OH)2 + 5H2O2 → S + SO42- + 2HS- + Mg2+ + 8H2O + 2H+
Magnesium Hydroxide X Aeration | 5H2S (aq) + Mg(OH)2 + 3O2 → 2S + SO42- + 2HS- + Mg2+ + 4H2O + 2H+
Volumetric air flow to treat a certain concentration of hydrogen sulfide.
Examples of combinations to raise pH and ORP.
  Treatments should be preventative and added before H2S formation in sewer lines
  Aeration is considered the cheapest, least hazardous, and easiest to handle
  Another potential solution to consider is adding a strong base to raise pH in combination with aeration for mixing as well as increase ORP
  Magnesium hydroxide is considered easiest and least hazardous chemical to raise pH
  Calcium nitrate is considered the preferred chemical electron acceptor for helping to raise ORP
  Hydrogen peroxide would be effective to prevent H2S formation, but has elevated hazardous handling and cost concerns
  Bench and pilot scale testing of proposed preventative treatment options should be implemented before final decision on treatment solution
  Past experiences in managing H2S treatments should still be considered in the current study
  The pilot testing program should begin with the easiest solution to implement before advancing to more sophisticated and costly solutions
  Treatments that combine raising pH and ORP should be given strong consideration
  The mixing of any chemical addition to the wastewater should be studied
Availability as a liquid treatment
Must be effective and remove H2S to below 0.5 mg/L
Minimal operation and maintenance
Needs to be cost efficient
Prefer the treatment not be hazardous and easy to contain in case of spill
Hypochlorite (OCl-) solutions can do both
Use aeration and a base to combine raising pH and ORP
Proprietary compounds that raise pH and ORP, e.g., base mixed with a permanganate
  The Greater Augusta Area has high levels of hydrogen sulfide (H2S) in their extended sewer lines
  Sulfur reducing bacteria (microbes) in the wastewater reduce sulfur compounds to hydrogen sulfide
  Hydrogen sulfide emits a pungent rotten egg odor that disturbs the public
  Hydrogen sulfide can be released from the wastewater and can develop sulfuric acid in the upper regions of the extended sewer lines, i.e., crown corrosion
  This project focused on various methods to control hydrogen sulfide in the extended sewer lines